## Slide 1: Parts of a Processor
A Level Computer Science – Unit 1

## Slide 2: Parts of a processor
Processor Components
What you need to know
Describe the function of the ALU and Control Unit

## Slide 3: Parts of a processor
The Central Processing Unit
The CPU, also known simply as the processor, has a number of different components which enable it to carry out its task of executing instructions.
These components include:
Control Unit
Buses
Arithmetic/logic unit (ALU)
Dedicated registers

## Slide 4: Parts of a processor
Control Unit
The Control Unit controls and coordinates the activities of the CPU, directing the flow of data between the CPU and other devices . It accepts the next instruction, decodes it into several sequential steps such as fetching addresses and data from memory, manages its execution and stores the resulting data back in memory or registers.

## Slide 5: Parts of a processor
Buses
A bus is a set of parallel wires connecting two or more components of a computer. It typically consists of 8,16,32 or 64 lines.
The processor is connected to main memory by three separate buses. When the CPU wishes to access a particular main memory location, it sends this address to memory on the address bus. The data in that location is then returned to the CPU on the data bus. Control signals are sent along the control bus.

## Slide 6: Parts of a processor
Buses

## Slide 7: Parts of a processor
Buses
In the previous figure, you can see that the data, address and control buses connect the processor, memory and I/O controllers (Input and Output). These three buses are known collectively as the system bus. Each bus is a shared transmission medium, so that only one device can transmit along a bus at any one time.
Data and control signals travel in both directions between the processor, memory and I/O controllers. Addresses, on the other hand, travel only one way along the address bus: the processor sends the address of an instruction, or of data to be stored or retrieved, to memory or to an I/O controller.
**The input/output controller is a device that interfaces between an input or output device and the computer or hardware device.

## Slide 8: Parts of a processor
Control Bus
The control bus is a bi-directional bus, meaning that signals ca be carried in bot directions. The data and address buses are shared by all components of the systems. Control lines must therefore be provided to ensure that access to and use of the data and address buses by the different components of the system does not lead to conflict.
The purpose of the control bus is to transmit command, timing and specific status information between system components.
Control lines include:
Bus Request – indicates that a device is requesting the use of the data bus
Bus Grant – indicates that the CPU has granted access to the data bus
Memory Write – causes data on the data bus to be written into the addressed location
Memory Read – causes data from the addressed location to be placed on the data bus
Interrupt Request – indicates that a device is requesting access to the CPU
Clock – used to synchronise operations

## Slide 9: Parts of a processor
Data Bus
The data bus, typically consisting of 8, 16, 32, 64 separate lines, provides a bi-directional path for moving data and instructions between system components

## Slide 10: Parts of a processor
Address Bus
Memory is divided up internally into units called words. A word is a fixed size group of digits, typically 16, 32 or 64 bits, which is handled as a unit by the processor, and different types of processor have different word sizes.
Each word in memory has its own specific address. The address bus transmits the memory addresses of words that are used as operations in program instructions, so that the data can be retrieved and sent back to the processor. When an instruction has been performed and the result is to be stored at a particular memory location, it is transmitted via the data bus.

## Slide 11: Parts of a processor
ALU – Arithmtic – Logic Unit
The ALU performs arithmetic and logical operations on the data. It can perform instructions such as ADD, SUBTRACT, MULTIPLY, DIVIDE on fixed or floating point numbers, It can also perform shift operations, shifting bits to the left or right within a register. It can carry out Boolean logic operations, comparing two values and using operations such as AND, OR, NOT, XOR.

## Slide 12: Parts of a processor
Registers
Registers are special memory cells that operate at very high speed. All arithmetic, logical or shift operations take place in registers and there are typically up to 16 general purpose registers in the CPU.
However, although most modern computers have many registers, some special-purpose processors still use a single accumulator, in order to simplify the design. The accumulator takes the place of the general purpose registers. For simplicity, we will assume that all calculations take place in a single register called the accumulator.

## Slide 13: Parts of a processor
Registers
Carrying out instructions one after the other requires many different pieces of information be held. As well as the accumulator, there are several other special purpose registers.
The program counter (PC), which holds the address of the next instruction to be executed. This may be the next instruction in a sequence of instructions, or, if the current instruction is a branch or jump instruction, the address to jump to, copied from the current instruction register (CIR) to the PC.
The current instruction register (CIR), which holds the current instructions being executed, divided into operand and opcode.
The memory address register (MAR) which holds the address of the memory location from which data (or an instruction) is to be fetched or to which data is to be written
The memory data register (MDR) which is used to temporally store the data read from or written to memory. It is sometimes known as the memory buffer register.
** operand - the quantity on which an operation is to be done.
** opcode - is the portion of a machine language instruction that specifies the operation to be performed

## Slide 14: Parts of a processor
Registers