## Slide 1: The Fetch-Decode-Execute Cycle
A Level Computer Science – Unit 1

## Slide 2: The Fetch-Decode-Execute Cycle
The sequence of operators involved in executing an instruction can be divided into three phases – fetching, decoding and executing it. This cycle is repeated over and over as each instruction of the program is executed.

## Slide 3: The Fetch-Decode-Execute Cycle

## Slide 4: The Fetch-Decode-Execute Cycle
How the registers are used in the Fetch – Execute cycle
Fetch Phase
The address of the next instruction is copied from the program counter (PC) to the memory address register (MAR)
The instruction held at that address is copied to the memory data register (MDR). Simultaneously, the content of the PC is incremented so that it holds the address of the next instruction.
The contents of the MDR are copied to the current instruction register (CIR)

## Slide 5: The Fetch-Decode-Execute Cycle
How the registers are used in the Fetch – Execute cycle
Decode Phase
4. The instruction in the CIR is decoded. The instruction is split into opcode and operand and the opcode is used to determine the type of instruction and what hardware to use to execute it. The operand hold either:
The address of the data to be used with the operation, which is then copied to the MAR or
The actual data to be operated on, which will be copied to the MDR
The data to be operated on may be passed to the ALU/accumulator
An opcode (abbreviated from operation code, also known as instruction syllable or opstring) is the portion of a machine language instruction that specifies the operation to be performed. Beside the opcode itself, most instructions also specify the data they will process, in the form of operands.

## Slide 6: The Fetch-Decode-Execute Cycle
How the registers are used in the Fetch – Execute cycle
Execute Phase
5. The appropriate instruction/opcode is carried out on the operand.