## Slide 1: Processor Performance
A Level Computer Science – Unit 1

## Slide 2: Processor Performance
Describe the factors affecting the performance of the CPU: Clock Speed, Number of Cores, Cache

## Slide 3: Processor Performance
Factors affecting the processor
  Clock Speed
  The number of cores, or duplicate processors, linked together on a single chip
  The amount and type of cache memory

## Slide 4: Processor Performance
Clock Speed
The system clock generates a series of signals, switching between 0 and 1 several million times per second and synchronising CPU operations. Each CPU operation starts as the clock changes from 0 to 1 (or in some systems from 1 to 0) and the CPU cannot perform operations faster than the clock cycle (the time the clock takes to go from 0 to 1 and back to 0).

## Slide 5: Processor Performance
Clock Speed
All processor activities begin on a clock pulse, although some activities may take more than one clock cycle to complete. One clock cycle per second = 1 Hertz (Hz), and clock speed is measured in Gigahertz (GHz), about 1 billion cycles per second. Typical speeds for a PC are between 2 and 4 GHz. The greater the clock speed, the faster instructions will be executed.

## Slide 6: Processor Performance
Number of Cores
In a traditional computer (von Neumann machine), instructions are fetched and executed one at a time in a serial manner. However, computers nowadays have multiple cores. A dual-core processor has two processors linked together in the same integrated circuit, and a quad-core processor computer has four linked processors.

## Slide 7: Processor Performance
Number of Cores
Each core is theoretically able to process a different instruction at the same time with its own fetch-execute cycle, making the processor two or even three times faster with a quad core chip. However, although a dual-core processor has twice the power, it does not always perform twice as fast, because the software may not always be able to take advantage of both processors.

## Slide 8: Processor Performance
Amount and type of cache memory
Cache is a small amount of expensive, very fast memory inside the CPU. When an instruction is fetched from main memory it is copied into the cache so if it is needed again soon after, it can be fetched form cache, which is much quicker than going back to the main memory. As cache fills up, unused instructions or data still being held are replaced with more recent ones.

## Slide 9: Processor Performance
Amount and type of cache memory
There are different “levels” of cache:
Level 1 cache is extremely fast but small (between 2 – 64KB)
Level 2 cache is fairly fast and medium sized (256KB – 2MB)
Some CPUs also have a Level 3 cache.