## Slide 1: Von Neumann, Harvard and contemporary processor architecture.
A Level Computer Science – Unit 1

## Slide 2: Processor Architecture
Objectives
  Describe von Neumann, Harvard and contemporary processor architecture

## Slide 3: Processor Architecture
Memory and the stored program concept
Computers as we know them were first built and developed in the 1940s and 50s, and two of the early pioneers were Alan Turing and John von Neumann. The von Neumann architecture specifies the basic components of the computer and processor in which a shared memory and bus is used for both data and instructions.

## Slide 4: Processor Architecture
The stored program concept can be defined as follows: machine code instructions are fetched and executed serially by a processor that performs arithmetic and logical operations.
A program must be resident in main memory to be executed
The machine code instructions are fetched from memory one at a time, decoded and executed in the processor
Virtually all computers today are built on this principle, and so the general structure as shown in the figure on the next slide which is sometimes referred to as the von Neumann machine.

## Slide 5: The von Neumann Machine
The von Neumann architecture uses only a single memory bus. This is relatively cheap, requiring less pins than the Harvard architecture, and simple to use because the programmer can place instructions or data anywhere throughout the available memory.
It does not permit multiple memory access.

## Slide 6: The von Neumann Machine
In a von Neumann machine, the same data bus is used to transfer both data and instructions. Similarly, a single address bus is used to transfer the addresses of the data and instructions. The same word length is used for all memory, whether it holds data or instructions.
a word is the unit that a machine uses when working with memory. For example, on a 32 bit machine, the word is 32 bits long and on a 64 bit is 64 bits long. The word size determines the address space.

## Slide 7: Harvard Architecture
The Harvard Architecture is a computer architecture with physically separate memories for instructions and data. Harvard architecture is used extensively with embedded Digital Signal Processing (DSP) systems. DSP applications include audio and speech signal processing, sonar and radar signal processing.
The two different memories can have different characteristics, for example, in embedded systems instructions may be held in read-only memory while data memory requires read-write memory.
In some systems, there is much more instruction memory than data memory so a larger word size is used for instructions
The instruction address bus may be wider than the data bus

## Slide 8: Harvard Architecture
Embedded systems include special-purpose computers built into devices often operating in real time, such as those used in navigation systems, traffic lights, aircraft flight control systems and simulators.
Harvard architecture can be faster than von Neumann architecture because data and instructions can be fetched in parallel instead of competing for the same bus.

## Slide 9: Comparison of von Neumann and Harvard Architecture
Von Neumann Architecture | Harvard Architecture
Used in conventional processors in PCs, servers and embedded systems with only control functions | Used in digital signal processing and in embedded systems, mobile communication systems, audio, speech and image processing systems
Data and programs share the same memory | Instructions and data are held in separate memories
One bus in used to transfer data and instructions | Parallel data and instruction buses may be used
Programs can be optimised in size | Programs tend to be large

## Slide 10: Contemporary Processor Architecture
Modern high-performance CPU chips incorporate aspects of both von Neumann and Harvard architecture. In one design, there is one main memory for holding both data and instructions, but CPU cache memory is divided into an instruction cache and a data cache. Harvard architecture is used as the CPU accesses the cache.