## Slide 1: Pipelining
A Level Computer Science – Unit 1

## Slide 2: Pipelining
Pipelining is a technique used by some processors to improve performance. Without pipelining, the steps in the Fetch-Execute cycle take place one after the other. While the next instruction is being fetched, the ALU, the arithmetic part of the processor, is idle.
Using pipelining, the computer architecture allows the next instructions to be fetched at the same time as the processor is performing arithmetic or logic operations, holding them in a buffer close to the processor until the instruction can be performed

## Slide 3: Pipelining
Processor pipelining is sometimes divided into an instruction pipeline and an arithmetic pipeline. The instruction pipeline consists of the stages in which an instruction is moved through the processor, including its being fetched, buffered and then executed. The arithmetic pipeline represents the parts of an arithmetic operation that can be broken down and overlapped as they are performed.
Pipelining is now common in microprocessors used in PCs. Intel’s Pentium chip uses pipelining to execute as many as six instructions simulateneously.

## Slide 4: Pipelining
Watch the car factory break down video