## Slide 1: Words and word size
A Level Computer Science – Unit 1

## Slide 2: Address Bus (Memory Bus)
Each word, or group of bytes, in memory has its own specific address. When the processor wishes to read a word of data from memory, it first puts the address of the desired word on the address bus. The width of the address bus determines the maximum possible memory capacity of the system.
For example, if the address bus consisted of only 8 lines, then the maximum address it could transmit would be (in binary) 11111111 or 255, giving a maximum memory capacity of 256 (including address 0). A system with a 32 –bit address bus can address 2³² (4,294,967,296) memory locations giving an addressable memory space of 4 GiB. (This is the memory capacity of an average PC in 2016)

## Slide 3: Data Bus
The data bus transmits the data held in a word of memory, between processor components and memory. The largest operand (which is either an address or an actual value) that can be held in a word is therefore related to the size of the data bus. If the data bus is 16 bits wide, a word cannot hold an integer greater than 2¹⁶ -1, or more than two characters. A wider data bus can transmit larger values, or more characters at a time, or allow more bits more instructions.

## Slide 4: How this relates to assembly language
The basic structure of a machine code instruction in a computer with a 16-bit word may take the format shown below:
Operation Code |  |  |  |  |  |  |  | Operand(s) |  |  |  |  |  |  | 
Basic machine operation |  |  |  |  |  | Addressing mode |  |  |  |  |  |  |  |  | 
0 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1

## Slide 5: How this relates to assembly language
In assembly language, the operation code (opcode) will be expressed as a mnemonic such as ADD, SUB, LDA (load into the accumulator) etc. With only six bits for the opcode, there cannot be more than 2⁶ different instructions. The operand has to be held in only 8 bits. This would clearly not be practical in a general purpose computer which is more likely to have a word size of 32, 64 or 128 bits.