## Slide 1: Input Devices
A Level Computer Science – Unit 1

## Slide 2: Starter - Input, output and storage
Sort the following devices into two categories “Input” and “Output” devices

## Slide 3: Starter - Input, output and storage
INPUT DEVICES

## Slide 4: Starter - Input, output and storage
OUTPUT Devices

## Slide 5: Starter - Input, output and storage
STORAGE Device!

## Slide 6: Starter - Input, output and storage
Discussion Point:
“Many devices are now both input and output devices such as touch screens and gaming keyboards.”
Can students justify this statement?

## Slide 7: Input Devices
Barcodes
Barcodes first started appearing on grocery items in the 1970s, and today they are used for identification in thousands of applications from tracking parcels, shipping cartons, passenger luggage, blood, tissue and organ products around the world to the sale of items in shops and the recording of the details of people attending events. Keeping track of anything accurately is now almost unimaginable without barcodes.

## Slide 8: Input Devices
Barcodes
There are two different types of barcode: linear barcodes and 2D barcodes such as the Quick Response (QR) code, which can hold more information than the 1D barcode.

## Slide 9: Input Devices
Barcodes
2D barcodes are used for example in ticketless entry to concert, or access through gates to board a Eurostar train or passenger airline. They are also used in mobile phone apps that enable the user to take a photo of the code which may then provide them with further information such as a map of their location, product details or a website URL.

## Slide 10: Input Devices
Barcode Readers
There are four different barcode readers available, each using slightly different technology for reading and decoding a barcode. The four types are:
Pen-type readers
Laser scanners
CCD readers
Camera based readers

## Slide 11: Input Devices
Pen-type readers
Pen-type readers consist of a light source and photodiode that are placed next to each other in the tip of a pen or wand. To read a bar code, the person holding the pen must move the tip of it across the bars at a relatively uniform speed. The photodiode measures the intensity of the light reflected back from the light source as the tip crosses each bar and space in the printed code.
The photodiode generates a waveform that is used to measure the widths of the bars and spaces in the bar code. Dark bars in the bar code absorb light and white spaces reflect light so that the voltage waveform generated by the photodiode is a representation of the bar and space pattern in the bar code. This waveform is decoded by the scanner in a manner similar to the way Morse code dots and dashes are decoded.

## Slide 12: Input Devices
Laser scanners
Laser scanners work the same way as pen type readers except that they use a laser beam as the light source and typically employ either a reciprocating mirror or a rotating prism to scan the laser beam back and forth across the bar code. As with the pen type reader, a photo-diode is used to measure the intensity of the light reflected back from the bar code. In both pen readers and laser scanners, the light emitted by the reader is rapidly varied in brightness with a data pattern and the photo-diode receive circuitry is designed to detect only signals with the same modulated pattern.

## Slide 13: Input Devices
Camera-based readers
A camera-based imaging scanner uses a camera and image processing techniques to decode a 1D or 2D bar code. An imaging scanner can read a barcode on any surface, printed or onscreen, and can also read a code that is damaged or poorly printed. They are used in multiple applications such as:
Age verification by scanning a driving licence
Couponing – 2D coupons can be emailed to customers
Event ticketing
Consumers can use a cell phone to scan a QR code which can, for example;
Display a catalogue of movies or DVDs
Play an MP3 when scanned
Display nutrition information about a product

## Slide 14: Input Devices
Digital Cameras
A digital camera uses a CCD or CMOS (Complementary Metal Oxide Semiconductor) sensor comprising millions of tiny light sensors arranged in a grid. The binary data from each sensor is recorded onto the camera’s memory card so that the image can be reproduced using suitable software at a computer.
A CCD sensor tends to produce higher quality images and they are used in higher end cameras. They are also more reliable since the technology has been around for much longer. This however, is at the cost of power consumption, using up to 100 times that of a CMOS sensor.

## Slide 15: Input Devices
Digital Cameras

## Slide 16: Input Devices
Mastercard to allow European customers to pay using a SELFIE
Mastercard is rolling out its biometric identity check for online payments
The technology will use facial recognition through the camera on devices
They will be required to blink to show the camera is looking at a real face
Customers will also be able to use the fingerprint scanner on some phones
It is being introduced in 12 countries including the UK, Germany, Spain, Belgium and Sweden following a series of trials in the US and Canada

## Slide 17: Input Devices

## Slide 18: Input Devices
Radio Frequency Identification (RFID)
Radio-frequency identification (RFID) uses electromagnetic fields to automatically identify and track tags attached to objects. The tags contain electronically stored information.
RFID tags are used in many industries, for example, an RFID tag attached to an automobile during production can be used to track its progress through the assembly line; RFID-tagged pharmaceuticals can be tracked through warehouses; and implanting RFID microchips in livestock and pets allows positive identification of animals
This technology uses both input and output – an input device to read the signal from an RFID chip, and output to transmit a signal from an active tag.

## Slide 19: Input Devices
Passive and Active Tags
Active tags are physically larger as they include a battery to power the tag so that it actively transmits a signal for a reader to pick up. These are used to track things likely to be read from further away, such as cars as they pass through a motorway toll booth or runners in a marathon as they pas mile markers.
Passive tags are much cheaper to produce as they do not have a battery. They rely on the radio waves emitted from a reader up to a metre away to provide enough electromagnetic power to the card using its coiled antenna. These are most common in tagging items such as groceries, music CDs, smart cards – e.g. contactless bank cards