## Slide 1: RAM and ROM
A Level Computer Science – Unit 1

## Slide 2: Starter
Sort the following statements into their respective categories
Random Access memory (RAM) Read Only Memory (ROM)
Usually quite large.
Not as large as hard disks.
Volatile.
Used to store programs and data in use by the processor. Programs include the operating system and applications software.
Allows fast access to data therefore speeds up the computer because it is solid state.
Usually quite small.
Non-volatile.
Used to store the boot program (bootstrap): a small program to load the operating system.
Used in embedded systems such as washing machines to store a program that can’t be changed.
Some of the BIOS may be stored here, but because it includes settings that change, not the whole BIOS.
Programs stored in in this or flash memory are known as firmware.
Operating systems on older computers that were not upgradable were stored this way.

## Slide 3: Starter - Answers

## Slide 4: Activity
1.Find out when and where these types of memory were used:
Magnetic core rope ROM
Magnetic core RAM
What is a “core dump”?

## Slide 5: Activity
Magnetic core rope ROM
First used in the 1960s by early NASA Mars probes and then in the Apollo Guidance Computer.
Magnetic core RAM
Magnetic core memory was the predominant form of random-access computer memory for 20 years between about 1955 and 1975. Such memory is often just called core memory, or, informally, core.
What is a “core dump”?
A core dump is a file that is saved containing a mirror image of what is in the RAM at the time. Traditionally used to assist in debugging when a program terminated unexpectedly. Today used to put your computer in sleep or hibernate.

## Slide 6: RAM and ROM
Computers have two kinds of internal memory: random access memory (RAM) and read-only memory (ROM).
RAM is used to store programs and data that are currently being used. It is volatile, meaning that its contents are lost when the computer is switched off.
ROM is used to hold information that needs to be permanently in memory. The bootstrap loader, for example, (the small program that starts up as soon as the computer is switched on and causes the operating system to be loaded) has to be held in ROM.
In embedded systems such as the software inside a washing machine, vehicle or camera, for example, never changes so is held in ROM.