## Slide 1: Output Devices
A Level Computer Science – Unit 1

## Slide 2: Starter
Look at the following pictures and label up all the input, output and storage devices you think are being used.
Remember to include “implied” devices, that is to say ones which you can logically work out must be present but which you might not necessarily be able to see in the photo.

## Slide 3: Starter

## Slide 4: Starter
Actuator
Hard Drive
LEDS
Monitor
Pressure Pads
Buttons
Speaker
Speaker

## Slide 5: Starter

## Slide 6: Starter
OCR
Keypad
Printer
Scanner
Actuator
Hard Drive
Chip and Pin
Speaker
Touchscreen
Barcode scanner
Speaker

## Slide 7: Output Devices
Output Devices
Describe how different output devices can be applied as a solution to different problems
Output devices take data produced by the computer and turn it into a form that humans can understand. This could be, for example, written or spoken text, an image on a screen, music or a multimedia presentation.
A different type of output device is a actuator, which might respond to an input signal to turn on a sprinkler, open or close a window in a greenhouse, or perform any number of actions.
Common output devices include screens, printers, multimedia projectors, speakers and actuators.

## Slide 8: Screens
LCD Monitors
Liquid crystal display (LCD) monitors contain groups of red, green and blue diodes to form each pixel. The screen is typically back-lit using light-emitting diodes (LEDs). These have several advantages over older technology:
They reach maximum brightness almost immediately
The image is sharper with more realistic and vivid colours
They produce a brighter light which leads to better picture definition
Since LEDs are very small, screens can be much thinner in construction
They last almost indefinitely which makes the screens much more reliable
They consume little power and produce little heat with low running costs

## Slide 9: Screens
Organic LED (OLED) Screens
These are brighter, thinner and lighter than traditional LCD or LED Screens. The screen is plastic rather than glass so they are flexible. OLED screens can be used wherever LCD screens are used, for TVs, computer screens, MP3 and mobile phone screens.
In the future they may be used to make inexpensive animated billboards, super-thin pages for electronic books or wearable technology.

## Slide 10: Screens
Organic LED (OLED) Screens (cont….)
when made of plastic – they are flexible – can be flexible enough to print onto clothing
They are much thinner
They are brighter and need no backlighting, so they consume less power, which translates into longer battery life in a portable device
LCDs can be slow to refresh (a problem in fast-moving sports or computer games), OLEDs respond up to 200 times faster
They produce truer colours through a much bigger viewing angle, unlike LCDs where the colours darken and disappear if you look from the side
One drawback is that the OLEDs do not last as long, tending to wear out around four times faster than LCDs. They are also very sensitive to water, which is a potential problem in a mobile phone.

## Slide 11: Printers
Laser Printers
Laser printers offer high-quality, high-speed printing. Their function is similar to that of a photocopier, using powered ink called toner.
This type of printer is becoming increasingly affordable and is frequently used as a home printer, in businesses and in professional printing services. Colour laser printers are far more expensive than black and white versions. They contain four toner cartridges (Cyan, Magenta, Yellow and Black or CMYK) and the paper must go through a process to the black-only printer four times: once for each colour.
The usage of laser printers for print jobs other than text is limited by the quality of the print produced, which at about 1200 dpi makes photorealistic prints impossible and best left to inkjet printers.

## Slide 12: Printers
Laser Printers
https://youtu.be/WB0HnXcW8qQ

## Slide 13: Printers
Inkjet Printers
Inkjet printers work by spraying minute dots of ink onto paper to create an image. Depending on the resolution of the model, the number of colour cartridges used and the quality of the paper being used, they can produce excellent, photo – realistic images. They are cheaper than laser printers but much slower, and the ink cartridges have to be replaced frequently.
Given the choice, it is preferable to use a laser printer when a lot of text needs to be printed, and an inkjet printer to produce high quality photographic images.

## Slide 14: Printers
Dot Matrix Printers
These are known a impact printers. The print head has a matrix of pins which strike the surface of the paper through an inked ribbon to form letters. These printers are useful when multi-part stationary is required (Multipart or multi-part stationery is paper that is blank, or pre-printed as a form to be completed), and they can operate in damp or dirty environments. However, they are noisy, slow and the print quality is poor.

## Slide 15: Printers
3D Printers
3D printers have been used to create car and aeroplane parts, medical equipment, prosthetic limbs, fashion accessories and a multitude of other items. They have even, controversially, been used to produce working firearms and other weapons.
They are used for creating spare parts for obsolete equipment and to produce prototypes of new products. They can be used in many situations where a one-off item is required, for example to fill in the missing parts of a dinosaur skeleton or a 2000-year old artefact.

## Slide 16: Multimedia Projectors
The benefits of a multimedia presentation:
Prior to these 20+ students would crowd around a desk looking at a small screen
Copying down notes from a chalk board
Easily place images to engage the class
Watching videos and live webcam footage
Teachers don’t have to re-write the same thing on the board every lesson. Projectors allow teachers/presenters to present text, graphics, audio and video on the screen, display images or videos from the Internet, display PC applications and use the screen interactively.

## Slide 17: Computer Speakers
PCs, smartphones and other portable devices generally have a basic inbuilt speaker which can be used to output music, voice or sound tracks from a video. High quality speakers can be bought separately and when in use, they disable the in built speakers
Apart from playing music and video soundtracks, uses include giving verbal instructions in a sat-nav system, reading text from the screen for visually impaired people, giving warning beeps and notification alerts (e.g when you receive an email)

## Slide 18: Actuators
Actuators are motors that are commonly used in conjunction with sensors to control a mechanism, for example:
Opening a window or valve
Starting or stopping a pump
Turning a wheel
Moving an aircraft aileron (An aileron (French for 'little wing') is a hinged flight control surface usually forming part of the trailing edge of each wing of a fixed-wing aircraft)
Controlling devices in a “smart home”