## Slide 1: Storage Devices - The uses of magnetic, flash and optical storage devices
A Level Computer Science – Unit 1

## Slide 2: Starter
Concise definitions!
Write a definition for the following three terms.
Each definition must be 16 words or less.
Each definition must make at least 3 valid points.

## Slide 3: Concise Definitions
Magnetic Storage
Optical Storage
Solid State Storage
Write definition here…
Write definition here…
Write definition here…

## Slide 4: Concise Definitions
Magnetic Storage
Optical Storage
Solid State Storage
Data recorded onto magnetic disks. Mechanical parts move over disks surface to read and write data.
Data recorded onto optical disks. Lasers read and write data. Highly portable.
Data recorded onto solid state memory chips. Very durable and fast, no mechanical moving parts needed.










## Slide 5: Guess the storage device game!

## Slide 6: Secondary Storage
The need for secondary storage
A computer’s primary store is Random Access Memory. Unlike RAM, secondary storage is not directly accessible to the processor and has slow Thier access speeds. Secondary storage, however, has the advantage that it retains its contents when the computer’s power is turned off. This includes the computer’s internal hard disk, optical media and solid state disks.
How storage devices store data
Hard disks, optical disks and solid states disks all use different methods to store data, but in each case, use a technique which allows them to create and maintain a toggle state without power to represent either a 1 or a 0.

## Slide 7: Secondary Storage
Hard Disk
A hard disk uses rigid rotating platters with magnetic material. Ferrous (iron) particles on the disk are polarised to become either a north or south state. This represents 0 and 1. The disk is divided into tracks in concentric circles, and each track is subdivided into sectors.
The disk spins very quickly at speeds of up to 10,000 RPM. Like an old record player, a drive head (like the needle on a record player) moves across the disk to access different tracks and sectors.
Data is read from or written to the disk as it passes under the drive head. When the drive head is not in use, it is parked to one side of the disk in order to prevent damage from movement. A hard disk may consist of several platters, each with its own drive head.
https://www.youtube.com/watch?v=kdmLvl1n82U

## Slide 8: Secondary Storage
Hard Disk
Although hard disks are less portable than optical or sold state media their huge capacity makes them very suitable for desktop purposes. Smaller, denser surface areas spinning under the read-write heads mean that newer 3.5 inch disks have capacities of up to 640GB.

## Slide 9: Secondary Storage
Optical Disk
3 formats:
Read-only (CD ROM)
Recordable (CD-R)
Rewritable (CD-RW)
An optical disk works by using a high powered laser to “burn” (change the chemical properties of) sections of its surface, making them less reflective. A laser at a lower power is used to read the disk by shining light onto the surface and a sensor is used to measure the amount of light that is reflected back.

## Slide 10: Secondary Storage
CD ROM
A read-only CD-ROM disk pressed during manufacture has pits in its surface. Those areas that have not been pitted, are called lands. At the point where a pit starts or ends, light is scattered and therefore not reflected so well. Reflective and non-reflective areas are read as 1s and 0s. There is only one single track on an optical disk, arranged as a tight spiral.

## Slide 11: Secondary Storage
CD ROM and Blu-Ray
CD-ROM holds about 700MB
Blu-Ray holds about 50GB
These disks are the same size; their added capacity is owing to the shorter wavelength in the laser they use. This creates much smaller pits, enabling a greater number to fit in the same space along the track and also means that the track can be more tightly wound, and therefore much longer.
Recordable disks use a reflective layer with a transparent dye coating that becomes less reflective when a spot laser “burns” a spot in the track.
Rewritable compact disks use a laser and a magnet in order to heat a spot on the disk and then set its state to become a 0 or a 1 using the magnet before it cools again. A DVD-RW uses a phase change alloy that can change between amorphous and crystalline states by changing the power of the laser beam.

## Slide 12: Secondary Storage
Solid-State Disk (SSD)
Solid state disks are packaged to look like hard disk drives, rectangular in shape and sized to match industry-standard dimensions for hard drives (typically 2.5 and 3.5 inches).

## Slide 13: Secondary Storage
Solid-State Disk (SSD)
Inside, instead of platters and a read-write head, there is an array of chips arranged on a board. These components are put into the standard size “housing” so that they fit into existing laptops and desktop PCs. Solid state memory comprises millions of NAND flash memory cells, and a controller that manages pages and blocks of memory.