## Slide 1
Assembly language (including following and writing programs with Little Man Computer)
Introduction to programming
Reverse engineer this program to assembly language mnemonics and then to a high level language:
1001 0000001
0011 0001010
1001 0000001
0011 0001011
0001 0001010
0011 0001100
1001 0000010
0000 0000000
Machine Code | Mnemonic | Instruction
0000 0000000 | HLT | End program (Halt)
0001 xxxxxxx | ADD | Add address to accumulator
0010 xxxxxxx | SUB | Subtract address from accumulator
0011 xxxxxxx | STA | Store accumulator to address
0101 xxxxxxx | LDA | Load address to accumulator
0110 xxxxxxx | BRA | Branch always
0111 xxxxxxx | BRZ | Branch if accumulator is zero
1000 xxxxxxx | BRP | Branch if accumulator is greater than or equal to zero
1001 0000001 | INP | Input from keyboard to accumulator
1001 0000010 | OUT | Output from accumulator to display