## Slide 1
SLR15 Boolean algebra
Karnaugh maps – part 1
Introduction to modelling, manipulating and simplifying Boolean expressions with Karnaugh maps

## Slide 2
A note about this video
This video introduces Karnaugh maps.
It assumes you are already familiar with the content of our previous video on Boolean logic.
If you have not seen it yet, we suggest you watch Define problems using Boolean logic first.

## Slide 3
The need to simplify Boolean expressions
Boolean expressions describe electric circuits in computer systems and selection statements in programming.
We can use logic gates to illustrate these electric circuits.
It is important to use as few expressions (gates/electric components) as possible to:
  Reduce the size of the circuit.
  Reduce the cost of manufacturing the circuit.
  Reduce the power consumption of the circuit.
  Execute instructions as quickly as possible by reducing the need to fetch variables from memory.

## Slide 4
Using a Karnaugh map to model expressions
Karnaugh maps provide a method of simplifying Boolean expressions.
A two-input Karnaugh map can be used to illustrate an expression with two variables.
Let’s look at how we can use a Karnaugh map to model the expression: A V B
One variable should be placed along the top of the map. It can be either A or B – it doesn’t matter.
The second variable is then placed down the side of the map.
Expression: A V B |  |  | 
A
B
A
A
B
B

## Slide 5
Using a Karnaugh map to model expressions
Karnaugh maps provide a method of simplifying Boolean expressions.
A two-input Karnaugh map can be used to illustrate an expression with two variables.
Let’s look at how we can use a Karnaugh map to model the expression: A V B
One variable should be placed along the top of the map. It can be either A or B – it doesn’t matter.
The second variable is then placed down the side of the map.
Both of the possible states for each variable are entered into the map.
Expression: A V B |  |  | 
 |  | A | A
B |  |  | 
B |  |  | 
A
B
0
1
0
1

## Slide 6
Using a Karnaugh map to model expressions
We now take each expression in turn, separated by OR symbols.
To put the variable A in the map, we find all cells where A is 1.
Expression: A V B |  |  | 
 |  | A | A
 |  | 0 | 1
B | 0 |  | 
B | 1 |  | 
A
B
A V B
OR
V

## Slide 7
Using a Karnaugh map to model expressions
We now take each expression in turn, separated by OR symbols.
To put the variable A in the map, we find all cells where A is 1.
The highlighted cells all represent situations where A is 1 – we put a 1 in each of them.
We ignore B at this stage.
Expression: A V B |  |  | 
 |  | A | A
 |  | 0 | 1
B | 0 |  | 
B | 1 |  | 
A
B
A V B
OR
V
1
1

## Slide 8
Using a Karnaugh map to model expressions
We now look at the next expression after the OR.
To the put the variable B in the map, we find all cells where B is 1.
Expression: A V B |  |  | 
 |  | A | A
 |  | 0 | 1
B | 0 |  | 1
B | 1 |  | 1
A
B
A V B
OR
V

## Slide 9
Using a Karnaugh map to model expressions
We now look at the next expression after the OR.
To the put the variable B in the map, we find all cells where B is 1.
The highlighted cells all represent situations where B is 1 – we put a 1 in each of them.
We ignore A at this stage.
Expression: A V B |  |  | 
 |  | A | A
 |  | 0 | 1
B | 0 |  | 1
B | 1 |  | 1
A
B
A V B
OR
V
1

## Slide 10
Using a Karnaugh map to model expressions
This Karnaugh map now illustrates the expression: A OR B
Expression: A V B |  |  | 
 |  | A | A
 |  | 0 | 1
B | 0 |  | 1
B | 1 | 1 | 1
A
B

## Slide 11
Using a Karnaugh map to model expressions
Let’s look at another example of an expression – this time, using a NOT operator: A V ¬B
We have started filling out the blank Karnaugh map as before.
Expression: A V ¬B |  |  | 
 |  | A | A
 |  | 0 | 1
B | 0 |  | 
B | 1 |  | 
A
B

## Slide 12
Using a Karnaugh map to model expressions
We now take each expression in turn, separated by OR symbols.
To put the variable A in the map, we find all cells where A is 1.
Expression: A V ¬B |  |  | 
 |  | A | A
 |  | 0 | 1
B | 0 |  | 
B | 1 |  | 
A
B
A V ¬B
OR
V

## Slide 13
Using a Karnaugh map to model expressions
We now take each expression in turn, separated by OR symbols.
To put the variable A in the map, we find all cells where A is 1.
The highlighted cells all represent situations where A is 1 – we put a 1 in each of them.
We ignore B at this stage.
Expression: A V ¬B |  |  | 
 |  | A | A
 |  | 0 | 1
B | 0 |  | 
B | 1 |  | 
A
B
A V ¬B
OR
V
1
1

## Slide 14
Using a Karnaugh map to model expressions
We now look at the next expression after the OR.
To the put the variable ¬B in the map, we find all cells where B is 0.
Expression: A V ¬B |  |  | 
 |  | A | A
 |  | 0 | 1
B | 0 |  | 1
B | 1 |  | 1
A
B
A V ¬B
OR
V

## Slide 15
Using a Karnaugh map to model expressions
We now look at the next expression after the OR.
To the put the variable ¬B in the map, we find all cells where B is 0.
The highlighted cells all represent situations situations where B is 0 – we put a 1 in each of them.
We ignore A at this stage.
Expression: A V ¬B |  |  | 
 |  | A | A
 |  | 0 | 1
B | 0 |  | 1
B | 1 |  | 1
A
B
A V ¬B
OR
V
1

## Slide 16
Using a Karnaugh map to model expressions
This Karnaugh map now illustrates the expression: A OR NOT B
Expression: A V ¬B |  |  | 
 |  | A | A
 |  | 0 | 1
B | 0 | 1 | 1
B | 1 |  | 1
A
B

## Slide 17
Using a Karnaugh map to model expressions
A few observations
Only a single 1 is put in a cell.
There is no need to put zeros in blank cells.
We take each part of an expression and use the OR symbol to separate the expression into different parts.
Expression: A V ¬B |  |  | 
 |  | A | A
 |  | 0 | 1
B | 0 | 1 | 1
B | 1 |  | 1
A
B

## Slide 18
Using a Karnaugh map to model expressions
A few observations
Only a single 1 is put in a cell.
There is no need to put zeros in blank cells.
We take each part of an expression and use the OR symbol to separate the expression into different parts.
We have put three instances of each variable make it easier to see where those variables are true or false.
In your exams, you will probably just see B/A once in the heading, as shown in the map on the right.
Expression: A V ¬B |  |  | 
 |  | A | A
 |  | 0 | 1
B | 0 | 1 | 1
B | 1 |  | 1
A
B
B\A | 0 | 1
0 | 1 | 1
1 |  | 1

## Slide 19
What is a Karnaugh map and how do I draw one?
Having watched this video, you should be able to answer the following key question.

## Slide 20
SLR15 Boolean algebra
Boolean Algebra cheat sheet

## Slide 22
student.craigndave.org