## Slide 1
SLR15 Boolean algebra
Karnaugh maps – part 2
Simplifying two-input Karnaugh maps

## Slide 2
A note about this video
This video covers simplifying Boolean expressions using Karnaugh maps. It assumes you are already familiar with the basics of Karnaugh maps.
If you have not seen it yet, we suggest you watch Karnaugh maps Part 1 first.

## Slide 3
Using a Karnaugh map to simplify Boolean expressions
The expression we are considering here is: A AND B OR A AND NOT B
We have already drawn a Karnaugh map with two variables – A across the top and B down the side.
We have also filled in the two possible states of each variable – so, A can be either 0 or 1, as can B.
Expression: A ∧ B V A ∧ ¬B |  |  | 
 |  | A | A
 |  | 0 | 1
B | 0 |  | 
B | 1 |  | 
A
B

## Slide 4
Using a Karnaugh map to simplify Boolean expressions
We now take each part of the expression in turn, separated by an OR symbol.
To put the expression A AND B into the map, we find all the cells where both A and B are 1.
Expression: A ∧ B V A ∧ ¬B |  |  | 
 |  | A | A
 |  | 0 | 1
B | 0 |  | 
B | 1 |  | 
A
B
A ∧ B V A ∧ ¬B
OR
V

## Slide 5
Using a Karnaugh map to simplify Boolean expressions
We now take each part of the expression in turn, separated by an OR symbol.
To put the expression A AND B into the map, we find all the cells where both A and B are 1.
There is only one location where this is the case – we put a 1 in this cell.
Expression: A ∧ B V A ∧ ¬B |  |  | 
 |  | A | A
 |  | 0 | 1
B | 0 |  | 
B | 1 |  | 
A
B
A ∧ B V A ∧ ¬B
OR
V
1

## Slide 6
Using a Karnaugh map to simplify Boolean expressions
We now look at the second part of the expression after the OR symbol.
To put A AND NOT B in the map, we find all cells where A is 1 and B is 0.
Expression: A ∧ B V A ∧ ¬B |  |  | 
 |  | A | A
 |  | 0 | 1
B | 0 |  | 
B | 1 |  | 1
A
B
A ∧ B V A ∧ ¬B
OR
V

## Slide 7
Using a Karnaugh map to simplify Boolean expressions
We now look at the second part of the expression after the OR symbol.
To put A AND NOT B in the map, we find all cells where A is 1 and B is 0.
Again, there is only one location where this is the case – we put a 1 in this cell.
Expression: A ∧ B V A ∧ ¬B |  |  | 
 |  | A | A
 |  | 0 | 1
B | 0 |  | 
B | 1 |  | 1
A
B
A ∧ B V A ∧ ¬B
OR
V
1

## Slide 8
Using a Karnaugh map to simplify Boolean expressions
This Karnaugh map now illustrates the expression A.
So, the expression A ∧ B V A ∧ ¬B can be simplified to just A.
Expression: A ∧ B V A ∧ ¬B |  |  | 
 |  | A | A
 |  | 0 | 1
B | 0 |  | 1
B | 1 |  | 1
A
B

## Slide 9
Using a Karnaugh map to simplify Boolean expressions
This Karnaugh map now illustrates the expression A.
So, the expression A ∧ B V A ∧ ¬B can be simplified to just A.
Consider that the original circuit contains a number of electric components (logic gates).
We now know we can simplify the circuit down to just a single line.
Doing so will reduce the number of components required, saving both money and power.
Expression: A ∧ B V A ∧ ¬B
A
B
Expression: A

## Slide 10
How can Karnaugh maps be used to simplify Boolean expressions?
Having watched this video, you should be able to answer the following key question.

## Slide 11
SLR15 Boolean algebra
Boolean Algebra cheat sheet

## Slide 13
student.craigndave.org