## Slide 1
SLR15 Boolean algebra
Karnaugh maps – part 3
Simplifying three-input Karnaugh maps

## Slide 2
A note about this video
This video covers simplifying three-input Boolean expressions using Karnaugh maps and other advanced techniques.
It assumes you are already familiar with the basics of Karnaugh maps.
If you have not seen them yet, we suggest you go back and watch:
  Karnaugh maps Part 1
  Karnaugh maps Part 2

## Slide 3
Using a Karnaugh map to simplify Boolean expressions with three variables
Karnaugh maps are a method of simplifying Boolean expressions.
A three-input Karnaugh map can be used to illustrate an expression with three variables.
The expression we want to simplify here is: ¬C ∧ B V A ∧ B V C
Expression: ¬C ∧ B V A ∧ B V C |  |  |  |  | 

## Slide 4
Using a Karnaugh map to simplify Boolean expressions with three variables
Karnaugh maps are a method of simplifying Boolean expressions.
A three-input Karnaugh map can be used to illustrate an expression with three variables.
The expression we want to simplify here is: ¬C ∧ B V A ∧ B V C
As we have three variables, we have to put two variables on one axis.
In this case, we have decided to put A and B across the top and C down the side, but we could have gone with any configuration we like.
Expression: ¬C ∧ B V A ∧ B V C |  |  |  |  | 
A B
A B
A B
A B
C
C
A B
C

## Slide 5
Using a Karnaugh map to simplify Boolean expressions with three variables
First, we fill in both of the possible states for the variable C.
Expression: ¬C ∧ B V A ∧ B V C |  |  |  |  | 
 |  | A B | A B | A B | A B
C |  |  |  |  | 
C |  |  |  |  | 
0
1
A B
C

## Slide 6
Using a Karnaugh map to simplify Boolean expressions with three variables
With two variables across the top of our map, we have four possible headings: 00, 01, 10, 11
You may be tempted to write them in this order. It would make sense, as we are counting up in binary from zero to three.
However, the order of the binary numbers in the headings matters – we cannot simply count up in binary.
As we move from one position to the next, we can only change a single digit at a time.
Expression: ¬C ∧ B V A ∧ B V C |  |  |  |  | 
 |  | A B | A B | A B | A B
C | 0 |  |  |  | 
C | 1 |  |  |  | 
0 0
0 1
1 0
1 1
A B
C

## Slide 7
Using a Karnaugh map to simplify Boolean expressions with three variables
In this example, as we move from column heading two to three, we have a situation where both digits have changed at the same time:
  The 0 changed to a 1
  The 1 changed to a 0
Expression: ¬C ∧ B V A ∧ B V C |  |  |  |  | 
 |  | A B | A B | A B | A B
C | 0 |  |  |  | 
C | 1 |  |  |  | 
0 0
0 1
1 0
1 1
A B
C

## Slide 8
Using a Karnaugh map to simplify Boolean expressions with three variables
In this example, as we move from column heading two to three, we have a situation where both digits have changed at the same time:
  The 0 changed to a 1
  The 1 changed to a 0
We can only change one digit at a time. We have fixed the issue now – only one digit is changing as we move from heading to heading. As long as you follow this rule, you will always have a valid Karnaugh map.
Here, we are using a sequence known as Gray codes. They won’t appear in the exam, but if you want to know more, we will mention them again at the end of this video.
Expression: ¬C ∧ B V A ∧ B V C |  |  |  |  | 
 |  | A B | A B | A B | A B
C | 0 |  |  |  | 
C | 1 |  |  |  | 
0 0
0 1
1 1
1 0
A B
C

## Slide 9
Using a Karnaugh map to simplify Boolean expressions with three variables
Now our Karnaugh map is ready, we will place the first part of the expression into it.
Remember, we separate the expressions using OR symbols.
Expression: ¬C ∧ B V A ∧ B V C |  |  |  |  | 
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C | 0 |  |  |  | 
C | 1 |  |  |  | 
¬C ∧ B V A ∧ B V C
OR
V
OR
V
A B
C

## Slide 10
Using a Karnaugh map to simplify Boolean expressions with three variables
Now our Karnaugh map is ready, we will place the first part of the expression into it.
Remember, we separate the expressions using OR symbols.
We are starting with NOT C AND B.
There are two cells in our map where C is 0 and B is 1 – we put 1s in both of these cells.
The expression we are looking at only contains the variables B and C, so we can ignore A at this stage.
Expression: ¬C ∧ B V A ∧ B V C |  |  |  |  | 
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C | 0 |  |  |  | 
C | 1 |  |  |  | 
¬C ∧ B V A ∧ B V C
OR
V
OR
V
1
1
A B
C

## Slide 11
Using a Karnaugh map to simplify Boolean expressions with three variables
We move onto the next part of the expression – in this case, A AND B.
To put A AND B in the map, we find all the cells where A is 1 and B is 1.
Expression: ¬C ∧ B V A ∧ B V C |  |  |  |  | 
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C | 0 |  | 1 | 1 | 
C | 1 |  |  |  | 
¬C ∧ B V A ∧ B V C
OR
V
OR
V
A B
C

## Slide 12
Using a Karnaugh map to simplify Boolean expressions with three variables
We move onto the next part of the expression – in this case, A AND B.
To put A AND B in the map, we find all the cells where A is 1 and B is 1.
There are two locations where this is the case – we put a 1 in these cells.
Expression: ¬C ∧ B V A ∧ B V C |  |  |  |  | 
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C | 0 |  | 1 | 1 | 
C | 1 |  |  |  | 
¬C ∧ B V A ∧ B V C
OR
V
OR
V
1
A B
C

## Slide 13
Using a Karnaugh map to simplify Boolean expressions with three variables
We now move onto the final part of the expression – in this case, C.
Expression: ¬C ∧ B V A ∧ B V C |  |  |  |  | 
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C | 0 |  | 1 | 1 | 
C | 1 |  |  | 1 | 
¬C ∧ B V A ∧ B V C
OR
V
OR
V
A B
C

## Slide 14
Using a Karnaugh map to simplify Boolean expressions with three variables
We now move onto the final part of the expression – in this case, C.
To put C in the map, we find all the cells where C is 1 – there are four cells where this is the case.
Remember, the only variable we are concerned with at the moment is C, so we can ignore A and B.
Expression: ¬C ∧ B V A ∧ B V C |  |  |  |  | 
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C | 0 |  | 1 | 1 | 
C | 1 |  |  | 1 | 
¬C ∧ B V A ∧ B V C
OR
V
OR
V
1
1
1
A B
C

## Slide 15
Using a Karnaugh map to simplify Boolean expressions with three variables
Now that we have placed all the parts of the expression into the map, we can simplify it by drawing boxes around the 1s.
There are rules you need to be aware of for drawing these boxes – let’s look at them now.
Expression: ¬C ∧ B V A ∧ B V C |  |  |  |  | 
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C | 0 |  | 1 | 1 | 
C | 1 | 1 | 1 | 1 | 1
A B
C

## Slide 16
Simplification rules
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C D | 0 0 |  | 1 | 1 | 1
C D | 0 1 | 1 | 1 | 1 | 1
C D | 1 1 |  | 1 | 1 | 1
C D | 1 0 | 1 |  | 1 | 1
Boxes must be rectangles or squares
Rule
1
A B
C D
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C D | 0 0 |  | 1 | 1 | 1
C D | 0 1 | 1 | 1 | 1 | 1
C D | 1 1 |  | 1 | 1 | 1
C D | 1 0 | 1 |  | 1 | 1
A B
C D

## Slide 17
Simplification rules
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C D | 0 0 |  | 1 | 1 | 1
C D | 0 1 | 1 | 1 | 1 | 1
C D | 1 1 |  | 1 | 1 | 1
C D | 1 0 | 1 |  | 1 | 1
No diagonal boxes
Rule
2
A B
C D
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C D | 0 0 |  | 1 | 1 | 1
C D | 0 1 | 1 | 1 | 1 | 1
C D | 1 1 |  | 1 | 1 | 1
C D | 1 0 | 1 |  | 1 | 1
A B
C D

## Slide 18
Simplification rules
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C D | 0 0 |  | 1 | 1 | 1
C D | 0 1 | 1 | 1 | 1 | 1
C D | 1 1 |  | 1 | 1 | 1
C D | 1 0 | 1 |  | 1 | 1
Boxes can only contain 1s
Rule
3
A B
C D
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C D | 0 0 |  | 1 | 1 | 1
C D | 0 1 | 1 | 1 | 1 | 1
C D | 1 1 |  | 1 | 1 | 1
C D | 1 0 | 1 |  | 1 | 1
A B
C D

## Slide 19
Simplification rules
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C D | 0 0 |  | 1 | 1 | 1
C D | 0 1 | 1 | 1 | 1 | 1
C D | 1 1 |  | 1 | 1 | 1
C D | 1 0 | 1 |  | 1 | 1
Boxes must be as large as possible
Rule
4
A B
C D
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C D | 0 0 |  | 1 | 1 | 1
C D | 0 1 | 1 | 1 | 1 | 1
C D | 1 1 |  | 1 | 1 | 1
C D | 1 0 | 1 |  | 1 | 1
A B
C D

## Slide 20
Simplification rules
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C D | 0 0 |  | 1 | 1 | 1
C D | 0 1 | 1 | 1 | 1 | 1
C D | 1 1 |  | 1 | 1 | 1
C D | 1 0 | 1 |  | 1 | 1
Boxes of 2n 1s: 1, 2, 4, 8 or 16 digits
Rule
5
A B
C D
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C D | 0 0 |  | 1 | 1 | 1
C D | 0 1 | 1 | 1 | 1 | 1
C D | 1 1 |  | 1 | 1 | 1
C D | 1 0 | 1 |  | 1 | 1
A B
C D

## Slide 21
Simplification rules
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C D | 0 0 |  | 1 | 1 | 1
C D | 0 1 | 1 | 1 | 1 | 1
C D | 1 1 |  | 1 | 1 | 1
C D | 1 0 | 1 |  | 1 | 1
Boxes can overlap
Rule
6
A B
C D
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C D | 0 0 |  | 1 | 1 | 1
C D | 0 1 | 1 | 1 | 1 | 1
C D | 1 1 |  | 1 | 1 | 1
C D | 1 0 | 1 |  | 1 | 1
A B
C D

## Slide 22
Simplification rules
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C D | 0 0 |  | 1 | 1 | 1
C D | 0 1 | 1 | 1 | 1 | 1
C D | 1 1 |  | 1 | 1 | 1
C D | 1 0 | 1 |  | 1 | 1
Smallest possible number of boxes
Rule
7
A B
C D
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C D | 0 0 |  | 1 | 1 | 1
C D | 0 1 | 1 | 1 | 1 | 1
C D | 1 1 |  | 1 | 1 | 1
C D | 1 0 | 1 |  | 1 | 1
A B
C D

## Slide 23
Using a Karnaugh map to simplify Boolean expressions with three variables
Considering all these rules, the best outcome is to draw two overlapping boxes, each around a group of four 1s, as shown here.
These two boxes will now allow us to simplify our Boolean expression.
Expression: ¬C ∧ B V A ∧ B V C |  |  |  |  | 
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C | 0 |  | 1 | 1 | 
C | 1 | 1 | 1 | 1 | 1
A B
C

## Slide 24
Using a Karnaugh map to simplify Boolean expressions with three variables
How do we determine the simplified expression from these boxes?
  Take each box in any order.
  Take each variable in any order.
  If the digit for the variable in the heading stays the same, keep the variable.
  If the digit for the variable in the heading changes, discard the variable.
  Let’s work through this example to ensure you understand it fully.
Expression: ¬C ∧ B V A ∧ B V C |  |  |  |  | 
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C | 0 |  | 1 | 1 | 
C | 1 | 1 | 1 | 1 | 1
A B
C

## Slide 25
Using a Karnaugh map to simplify Boolean expressions with three variables
How do we determine the simplified expression from these boxes?
  Take each box in any order.
  Take each variable in any order.
  If the digit for the variable in the heading stays the same, keep the variable.
  If the digit for the variable in the heading changes, discard the variable.
  In this case, we have chosen this square to start off.
Expression: ¬C ∧ B V A ∧ B V C |  |  |  |  | 
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C | 0 |  | 1 | 1 | 
C | 1 | 1 | 1 | 1 | 1
A B
C

## Slide 26
Using a Karnaugh map to simplify Boolean expressions with three variables
How do we determine the simplified expression from these boxes?
  Take each box in any order.
  Take each variable in any order.
  If the digit for the variable in the heading stays the same, keep the variable.
  If the digit for the variable in the heading changes, discard the variable.
  In this case, we have chosen this square to start off.
  We have decided to start with A.
Expression: ¬C ∧ B V A ∧ B V C |  |  |  |  | 
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C | 0 |  | 1 | 1 | 
C | 1 | 1 | 1 | 1 | 1
A B
C

## Slide 27
Using a Karnaugh map to simplify Boolean expressions with three variables
How do we determine the simplified expression from these boxes?
  Take each box in any order.
  Take each variable in any order.
  If the digit for the variable in the heading stays the same, keep the variable.
  If the digit for the variable in the heading changes, discard the variable.
  In this case, we have chosen the square to start off.
  We have decided to start with A.
  The digit in the heading changes from 0 to 1, so we discard A.
Expression: ¬C ∧ B V A ∧ B V C |  |  |  |  | 
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C | 0 |  | 1 | 1 | 
C | 1 | 1 | 1 | 1 | 1
A B
C
Variable A – Discard

## Slide 28
Using a Karnaugh map to simplify Boolean expressions with three variables
How do we determine the simplified expression from these boxes?
  Take each box in any order.
  Take each variable in any order.
  If the digit for the variable in the heading stays the same, keep the variable.
  If the digit for the variable in the heading changes, discard the variable.
  We now look at the next variable, B.
Expression: ¬C ∧ B V A ∧ B V C |  |  |  |  | 
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C | 0 |  | 1 | 1 | 
C | 1 | 1 | 1 | 1 | 1
A B
C
Variable A – Discard

## Slide 29
Using a Karnaugh map to simplify Boolean expressions with three variables
How do we determine the simplified expression from these boxes?
  Take each box in any order.
  Take each variable in any order.
  If the digit for the variable in the heading stays the same, keep the variable.
  If the digit for the variable in the heading changes, discard the variable.
  We now look at the next variable, B.
  The digit in the heading stays the same – it is 1 in both cases – so we can keep B.
Expression: ¬C ∧ B V A ∧ B V C |  |  |  |  | 
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C | 0 |  | 1 | 1 | 
C | 1 | 1 | 1 | 1 | 1
A B
C
Variable A – Discard
Variable B – Keep

## Slide 30
Using a Karnaugh map to simplify Boolean expressions with three variables
How do we determine the simplified expression from these boxes?
  Take each box in any order.
  Take each variable in any order.
  If the digit for the variable in the heading stays the same, keep the variable.
  If the digit for the variable in the heading changes, discard the variable.
  We move to the final variable for the current box – in this case, C.
Expression: ¬C ∧ B V A ∧ B V C |  |  |  |  | 
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C | 0 |  | 1 | 1 | 
C | 1 | 1 | 1 | 1 | 1
A B
C
Variable A – Discard
Variable B – Keep

## Slide 31
Using a Karnaugh map to simplify Boolean expressions with three variables
How do we determine the simplified expression from these boxes?
  Take each box in any order.
  Take each variable in any order.
  If the digit for the variable in the heading stays the same, keep the variable.
  If the digit for the variable in the heading changes, discard the variable.
  We move to the final variable for the current box – in this case, C.
  The digit in the heading changes from 0 to 1, so we discard C.
Expression: ¬C ∧ B V A ∧ B V C |  |  |  |  | 
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C | 0 |  | 1 | 1 | 
C | 1 | 1 | 1 | 1 | 1
A B
C
Variable A – Discard
Variable B – Keep
Variable C – Discard

## Slide 32
Using a Karnaugh map to simplify Boolean expressions with three variables
How do we determine the simplified expression from these boxes?
  Take each box in any order.
  Take each variable in any order.
  If the digit for the variable in the heading stays the same, keep the variable.
  If the digit for the variable in the heading changes, discard the variable.
  We have considered all the variables for the first box, and the only one we are keeping is B.
  We now know this entire box can be simplified down to just B.
Expression: ¬C ∧ B V A ∧ B V C |  |  |  |  | 
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C | 0 |  | 1 | 1 | 
C | 1 | 1 | 1 | 1 | 1
A B
C
Variable A – Discard
Variable B – Keep
Variable C – Discard
B

## Slide 33
Using a Karnaugh map to simplify Boolean expressions with three variables
How do we determine the simplified expression from these boxes?
  Take each box in any order.
  Take each variable in any order.
  If the digit for the variable in the heading stays the same, keep the variable.
  If the digit for the variable in the heading changes, discard the variable.
  We now move onto the other box.
Expression: ¬C ∧ B V A ∧ B V C |  |  |  |  | 
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C | 0 |  | 1 | 1 | 
C | 1 | 1 | 1 | 1 | 1
A B
C
B

## Slide 34
Using a Karnaugh map to simplify Boolean expressions with three variables
How do we determine the simplified expression from these boxes?
  Take each box in any order.
  Take each variable in any order.
  If the digit for the variable in the heading stays the same, keep the variable.
  If the digit for the variable in the heading changes, discard the variable.
  We now move onto the other box.
  Take each variable in turn – we have decided to start with A again.
Expression: ¬C ∧ B V A ∧ B V C |  |  |  |  | 
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C | 0 |  | 1 | 1 | 
C | 1 | 1 | 1 | 1 | 1
A B
C
B

## Slide 35
Using a Karnaugh map to simplify Boolean expressions with three variables
How do we determine the simplified expression from these boxes?
  Take each box in any order.
  Take each variable in any order.
  If the digit for the variable in the heading stays the same, keep the variable.
  If the digit for the variable in the heading changes, discard the variable.
  We now move onto the other box.
  Take each variable in turn – we have decided to start with A again.
  The digit in the heading changes from 0 to 1, so we discard A.
Expression: ¬C ∧ B V A ∧ B V C |  |  |  |  | 
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C | 0 |  | 1 | 1 | 
C | 1 | 1 | 1 | 1 | 1
A B
C
B
Variable A – Discard

## Slide 36
Using a Karnaugh map to simplify Boolean expressions with three variables
How do we determine the simplified expression from these boxes?
  Take each box in any order.
  Take each variable in any order.
  If the digit for the variable in the heading stays the same, keep the variable.
  If the digit for the variable in the heading changes, discard the variable.
  We now look at the next variable, B.
Expression: ¬C ∧ B V A ∧ B V C |  |  |  |  | 
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C | 0 |  | 1 | 1 | 
C | 1 | 1 | 1 | 1 | 1
A B
C
B
Variable A – Discard

## Slide 37
Using a Karnaugh map to simplify Boolean expressions with three variables
How do we determine the simplified expression from these boxes?
  Take each box in any order.
  Take each variable in any order.
  If the digit for the variable in the heading stays the same, keep the variable.
  If the digit for the variable in the heading changes, discard the variable.
  We now look at the next variable, B.
  Once again, the digit in the heading changes from 0 to 1, so we also discard B.
Expression: ¬C ∧ B V A ∧ B V C |  |  |  |  | 
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C | 0 |  | 1 | 1 | 
C | 1 | 1 | 1 | 1 | 1
A B
C
B
Variable A – Discard
Variable B – Discard

## Slide 38
Using a Karnaugh map to simplify Boolean expressions with three variables
How do we determine the simplified expression from these boxes?
  Take each box in any order.
  Take each variable in any order.
  If the digit for the variable in the heading stays the same, keep the variable.
  If the digit for the variable in the heading changes, discard the variable.
  We move to the final variable for the current box – in this case, C.
Expression: ¬C ∧ B V A ∧ B V C |  |  |  |  | 
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C | 0 |  | 1 | 1 | 
C | 1 | 1 | 1 | 1 | 1
A B
C
B
Variable A – Discard
Variable B – Discard

## Slide 39
Using a Karnaugh map to simplify Boolean expressions with three variables
How do we determine the simplified expression from these boxes?
  Take each box in any order.
  Take each variable in any order.
  If the digit for the variable in the heading stays the same, keep the variable.
  If the digit for the variable in the heading changes, discard the variable.
  We move to the final variable for the current box – in this case, C.
  There is only one heading to consider in this case, so it cannot change – we keep C.
Expression: ¬C ∧ B V A ∧ B V C |  |  |  |  | 
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C | 0 |  | 1 | 1 | 
C | 1 | 1 | 1 | 1 | 1
A B
C
B
Variable A – Discard
Variable B – Discard
Variable C – Keep

## Slide 40
Using a Karnaugh map to simplify Boolean expressions with three variables
How do we determine the simplified expression from these boxes?
  Take each box in any order.
  Take each variable in any order.
  If the digit for the variable in the heading stays the same, keep the variable.
  If the digit for the variable in the heading changes, discard the variable.
  We have considered all the variables for this box, and the only one we are keeping is C.
Expression: ¬C ∧ B V A ∧ B V C |  |  |  |  | 
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C | 0 |  | 1 | 1 | 
C | 1 | 1 | 1 | 1 | 1
A B
C
B
Variable A – Discard
Variable B – Discard
Variable C – Keep
C

## Slide 41
Using a Karnaugh map to simplify Boolean expressions with three variables
So, the first box represents B.
The second box represents C.
Different parts of the original expression (the different boxes we are looking at) are separated by ORs.
Using our Karnaugh map, we have simplified the original expression (¬C ∧ B V A ∧ B V C) to: B V C
  You could also write it as: C V B
  The order of the expressions either side of an OR doesn’t matter – this is known as the law of commutation.
Expression: ¬C ∧ B V A ∧ B V C |  |  |  |  | 
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C | 0 |  | 1 | 1 | 
C | 1 | 1 | 1 | 1 | 1
A B
C
B
C
B
C
V
Simplified expression:

## Slide 42
Using a Karnaugh map to simplify Boolean expressions with three variables
Let’s look at another example and simplify: ¬B V A ∧ B ∧ C
We will start by drawing up a blank Karnaugh map. We have:
  Placed variables A and B across the top.
  Placed C down the side.
  Added binary number headings representing the different states of the variables.
Remember, when writing out the headings, we are not counting up in binary – we have to make sure only one digit changes at a time.
Expression: ¬B V A ∧ B ∧ C |  |  |  |  | 
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C | 0 |  |  |  | 
C | 1 |  |  |  | 
A B
C

## Slide 43
Using a Karnaugh map to simplify Boolean expressions with three variables
Now our Karnaugh map is ready, we will place the first part of the expression into it.
Remember, we separate the different parts of the expression with OR symbols.
Expression: ¬B V A ∧ B ∧ C |  |  |  |  | 
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C | 0 |  |  |  | 
C | 1 |  |  |  | 
A B
C
¬B V A ∧ B ∧ C
OR
V

## Slide 44
Using a Karnaugh map to simplify Boolean expressions with three variables
Now our Karnaugh map is ready, we will place the first part of the expression into it.
Remember, we separate the different parts of the expression with OR symbols.
We are starting with NOT B.
There are four cells where B is 0 – we put 1s in these cells.
Expression: ¬B V A ∧ B ∧ C |  |  |  |  | 
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C | 0 |  |  |  | 
C | 1 |  |  |  | 
A B
C
¬B V A ∧ B ∧ C
OR
V
1
1
1
1

## Slide 45
Using a Karnaugh map to simplify Boolean expressions with three variables
We now move onto the next part of our expression – in this case: A AND B AND C
To put A AND B AND C in the map, we need to find all the cells where A, B and C are all 1.
Expression: ¬B V A ∧ B ∧ C |  |  |  |  | 
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C | 0 | 1 |  |  | 1
C | 1 | 1 |  |  | 1
A B
C
¬B V A ∧ B ∧ C
OR
V

## Slide 46
Using a Karnaugh map to simplify Boolean expressions with three variables
We now move onto the next part of our expression – in this case: A AND B AND C
To put A AND B AND C in the map, we need to find all the cells where A, B and C are all 1.
There is only one cell where this is the case – we put a 1 in this cell.
Expression: ¬B V A ∧ B ∧ C |  |  |  |  | 
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C | 0 | 1 |  |  | 1
C | 1 | 1 |  |  | 1
A B
C
¬B V A ∧ B ∧ C
OR
V
1

## Slide 47
Using a Karnaugh map to simplify Boolean expressions with three variables
Now we have placed all the parts of the expression into the map, we can simplify it by drawing boxes around the 1s making sure to remember the rules for doing so:
  Boxes must be rectangles or squares.
  No diagonal boxes
  Boxes can only contain 1s.
  Boxes must be as large as possible.
  Boxes of 2n 1s: 1, 2, 4, 8 or 16 digits.
  Boxes can overlap.
  Smallest possible number of boxes.
Expression: ¬B V A ∧ B ∧ C |  |  |  |  | 
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C | 0 | 1 |  |  | 1
C | 1 | 1 |  | 1 | 1
A B
C

## Slide 48
Using a Karnaugh map to simplify Boolean expressions with three variables
At this point, you may be tempted to draw the two boxes shown here.
Expression: ¬B V A ∧ B ∧ C |  |  |  |  | 
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C | 0 | 1 |  |  | 1
C | 1 | 1 |  | 1 | 1
A B
C

## Slide 49
Using a Karnaugh map to simplify Boolean expressions with three variables
At this point, you may be tempted to draw the two boxes shown here.
However, there is one additional rule we have not yet covered – boxes can wrap around the map.
Expression: ¬B V A ∧ B ∧ C |  |  |  |  | 
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C | 0 | 1 |  |  | 1
C | 1 | 1 |  | 1 | 1
A B
C

## Slide 50
Using a Karnaugh map to simplify Boolean expressions with three variables
Let’s look at the implications of this extra rule now.
The most complex Karnaugh map you will see has four variables, as shown here.
The wrapping rule means boxes can wrap around the left, right, top and bottom edges.
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C D | 0 0 | 1 |  |  | 1
C D | 0 1 |  |  |  | 
C D | 1 1 |  |  |  | 
C D | 1 0 | 1 |  |  | 1
A B
C D

## Slide 51
Using a Karnaugh map to simplify Boolean expressions with three variables
Let’s look at the implications of this extra rule now.
The most complex Karnaugh map you will see has four variables, as shown here.
The wrapping rule means boxes can wrap around the left, right, top and bottom edges.
In this example, that means we actually have a single box that wraps around all four corners.
Although we represent a Karnaugh map as a 2D grid, it is actually more accurate to think of it as a torus – a 3D donut-shaped object.
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C D | 0 0 | 1 |  |  | 1
C D | 0 1 |  |  |  | 
C D | 1 1 |  |  |  | 
C D | 1 0 | 1 |  |  | 1
A B
C D

## Slide 52
Using a Karnaugh map to simplify Boolean expressions with three variables
Looking at a Karnaugh map this way, you can see how the four corners are, in reality, all next to each other and form a single square.

## Slide 53
Using a Karnaugh map to simplify Boolean expressions with three variables
To put it another way, we can move off any edge of a Karnaugh map and it continues on the opposite edge.

## Slide 54
Using a Karnaugh map to simplify Boolean expressions with three variables
Back to our example, now we’ve covered wrapping, we now see that one of our boxes will look like this.
Expression: ¬B V A ∧ B ∧ C |  |  |  |  | 
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C | 0 | 1 |  |  | 1
C | 1 | 1 |  | 1 | 1
A B
C

## Slide 55
Using a Karnaugh map to simplify Boolean expressions with three variables
Knowing this new rule, you might be tempted to draw your second box as shown here.
However, we can’t do that, as one of the rules states we need boxes that contain 2n 1s.
This box would give us a group of three 1s when we need two or four.
Expression: ¬B V A ∧ B ∧ C |  |  |  |  | 
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C | 0 | 1 |  |  | 1
C | 1 | 1 |  | 1 | 1
A B
C

## Slide 56
Using a Karnaugh map to simplify Boolean expressions with three variables
Given all these rules, the most optimal outcome is shown here.
These two boxes will now allow us to simplify the original expression.
Expression: ¬B V A ∧ B ∧ C |  |  |  |  | 
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C | 0 | 1 |  |  | 1
C | 1 | 1 |  | 1 | 1
A B
C

## Slide 57
Using a Karnaugh map to simplify Boolean expressions with three variables
How do we determine the simplified expression from these boxes?
  Take each box in any order.
  Take each variable in any order.
  If the digit for the variable in the heading stays the same, keep the variable.
  If the digit for the variable in the heading changes, discard the variable.
  We can choose either box to start with – we have chosen the wrap-around square.
Expression: ¬B V A ∧ B ∧ C |  |  |  |  | 
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C | 0 | 1 |  |  | 1
C | 1 | 1 |  | 1 | 1
A B
C

## Slide 58
Using a Karnaugh map to simplify Boolean expressions with three variables
How do we determine the simplified expression from these boxes?
  Take each box in any order.
  Take each variable in any order.
  If the digit for the variable in the heading stays the same, keep the variable.
  If the digit for the variable in the heading changes, discard the variable.
  We can choose either box to start with – we have chosen the wrap-around square.
  Take each variable in turn – we have decided to start with A.
Expression: ¬B V A ∧ B ∧ C |  |  |  |  | 
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C | 0 | 1 |  |  | 1
C | 1 | 1 |  | 1 | 1
A B
C

## Slide 59
Using a Karnaugh map to simplify Boolean expressions with three variables
How do we determine the simplified expression from these boxes?
  Take each box in any order.
  Take each variable in any order.
  If the digit for the variable in the heading stays the same, keep the variable.
  If the digit for the variable in the heading changes, discard the variable.
  We can choose either box to start with – we have chosen the wrap-around square.
  Take each variable in turn – we have decided to start with A.
  The digit in the heading changes from 0 to 1, so we discard A.
Expression: ¬B V A ∧ B ∧ C |  |  |  |  | 
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C | 0 | 1 |  |  | 1
C | 1 | 1 |  | 1 | 1
A B
C
Variable A – Discard

## Slide 60
Using a Karnaugh map to simplify Boolean expressions with three variables
How do we determine the simplified expression from these boxes?
  Take each box in any order.
  Take each variable in any order.
  If the digit for the variable in the heading stays the same, keep the variable.
  If the digit for the variable in the heading changes, discard the variable.
  We now look at the next variable, B.
Expression: ¬B V A ∧ B ∧ C |  |  |  |  | 
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C | 0 | 1 |  |  | 1
C | 1 | 1 |  | 1 | 1
A B
C
Variable A – Discard

## Slide 61
Using a Karnaugh map to simplify Boolean expressions with three variables
How do we determine the simplified expression from these boxes?
  Take each box in any order.
  Take each variable in any order.
  If the digit for the variable in the heading stays the same, keep the variable.
  If the digit for the variable in the heading changes, discard the variable.
  We now look at the next variable, B.
  The digit in the heading stays the same – it is 0 in both cases – so we can keep ¬B.
Expression: ¬B V A ∧ B ∧ C |  |  |  |  | 
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C | 0 | 1 |  |  | 1
C | 1 | 1 |  | 1 | 1
A B
C
Variable A – Discard
Variable ¬B – Keep

## Slide 62
Using a Karnaugh map to simplify Boolean expressions with three variables
How do we determine the simplified expression from these boxes?
  Take each box in any order.
  Take each variable in any order.
  If the digit for the variable in the heading stays the same, keep the variable.
  If the digit for the variable in the heading changes, discard the variable.
  We move to the final variable for the current box – in this case, C.
Expression: ¬B V A ∧ B ∧ C |  |  |  |  | 
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C | 0 | 1 |  |  | 1
C | 1 | 1 |  | 1 | 1
A B
C
Variable A – Discard
Variable ¬B – Keep

## Slide 63
Using a Karnaugh map to simplify Boolean expressions with three variables
How do we determine the simplified expression from these boxes?
  Take each box in any order.
  Take each variable in any order.
  If the digit for the variable in the heading stays the same, keep the variable.
  If the digit for the variable in the heading changes, discard the variable.
  We move to the final variable for the current box – in this case, C.
  The digit in the heading changes from 0 to 1, so we discard C.
Expression: ¬B V A ∧ B ∧ C |  |  |  |  | 
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C | 0 | 1 |  |  | 1
C | 1 | 1 |  | 1 | 1
A B
C
Variable A – Discard
Variable ¬B – Keep
Variable C – Discard

## Slide 64
Using a Karnaugh map to simplify Boolean expressions with three variables
How do we determine the simplified expression from these boxes?
  Take each box in any order.
  Take each variable in any order.
  If the digit for the variable in the heading stays the same, keep the variable.
  If the digit for the variable in the heading changes, discard the variable.
  We have considered all the variables for the first box, and the only variable we are keeping is ¬B.
  We now know this entire box can be simplified down to just ¬B.
Expression: ¬B V A ∧ B ∧ C |  |  |  |  | 
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C | 0 | 1 |  |  | 1
C | 1 | 1 |  | 1 | 1
A B
C
Variable A – Discard
Variable ¬B – Keep
Variable C – Discard
¬B

## Slide 65
Using a Karnaugh map to simplify Boolean expressions with three variables
How do we determine the simplified expression from these boxes?
  Take each box in any order.
  Take each variable in any order.
  If the digit for the variable in the heading stays the same, keep the variable.
  If the digit for the variable in the heading changes, discard the variable.
  We now move onto the other box.
Expression: ¬B V A ∧ B ∧ C |  |  |  |  | 
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C | 0 | 1 |  |  | 1
C | 1 | 1 |  | 1 | 1
A B
C
¬B

## Slide 66
Using a Karnaugh map to simplify Boolean expressions with three variables
How do we determine the simplified expression from these boxes?
  Take each box in any order.
  Take each variable in any order.
  If the digit for the variable in the heading stays the same, keep the variable.
  If the digit for the variable in the heading changes, discard the variable.
  We now move onto the other box.
  Take each variable in turn – we have decided to start with A again.
Expression: ¬B V A ∧ B ∧ C |  |  |  |  | 
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C | 0 | 1 |  |  | 1
C | 1 | 1 |  | 1 | 1
A B
C
¬B

## Slide 67
Using a Karnaugh map to simplify Boolean expressions with three variables
How do we determine the simplified expression from these boxes?
  Take each box in any order.
  Take each variable in any order.
  If the digit for the variable in the heading stays the same, keep the variable.
  If the digit for the variable in the heading changes, discard the variable.
  We now move onto the other box.
  Take each variable in turn – we have decided to start with A again.
  The digit in the heading stays the same – it is 1 in both cases – so we can keep A.
Expression: ¬B V A ∧ B ∧ C |  |  |  |  | 
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C | 0 | 1 |  |  | 1
C | 1 | 1 |  | 1 | 1
A B
C
¬B
Variable A – Keep

## Slide 68
Using a Karnaugh map to simplify Boolean expressions with three variables
How do we determine the simplified expression from these boxes?
  Take each box in any order.
  Take each variable in any order.
  If the digit for the variable in the heading stays the same, keep the variable.
  If the digit for the variable in the heading changes, discard the variable.
  We now look at the next variable, B.
Expression: ¬B V A ∧ B ∧ C |  |  |  |  | 
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C | 0 | 1 |  |  | 1
C | 1 | 1 |  | 1 | 1
A B
C
¬B
Variable A – Keep

## Slide 69
Using a Karnaugh map to simplify Boolean expressions with three variables
How do we determine the simplified expression from these boxes?
  Take each box in any order.
  Take each variable in any order.
  If the digit for the variable in the heading stays the same, keep the variable.
  If the digit for the variable in the heading changes, discard the variable.
  We now look at the next variable, B.
  The digit in the heading changes from 1 to 0, so we discard B.
Expression: ¬B V A ∧ B ∧ C |  |  |  |  | 
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C | 0 | 1 |  |  | 1
C | 1 | 1 |  | 1 | 1
A B
C
¬B
Variable A – Keep
Variable B – Discard

## Slide 70
Using a Karnaugh map to simplify Boolean expressions with three variables
How do we determine the simplified expression from these boxes?
  Take each box in any order.
  Take each variable in any order.
  If the digit for the variable in the heading stays the same, keep the variable.
  If the digit for the variable in the heading changes, discard the variable.
  We move onto the final variable for the current box – in this case, C.
Expression: ¬B V A ∧ B ∧ C |  |  |  |  | 
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C | 0 | 1 |  |  | 1
C | 1 | 1 |  | 1 | 1
A B
C
¬B
Variable A – Keep
Variable B – Discard

## Slide 71
Using a Karnaugh map to simplify Boolean expressions with three variables
How do we determine the simplified expression from these boxes?
  Take each box in any order.
  Take each variable in any order.
  If the digit for the variable in the heading stays the same, keep the variable.
  If the digit for the variable in the heading changes, discard the variable.
  We move onto the final variable for the current box – in this case, C.
  There is only one heading to consider in this case, so it cannot change – we keep C.
Expression: ¬B V A ∧ B ∧ C |  |  |  |  | 
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C | 0 | 1 |  |  | 1
C | 1 | 1 |  | 1 | 1
A B
C
¬B
Variable A – Keep
Variable B – Discard
Variable C – Keep

## Slide 72
Using a Karnaugh map to simplify Boolean expressions with three variables
How do we determine the simplified expression from these boxes?
  Take each box in any order.
  Take each variable in any order.
  If the digit for the variable in the heading stays the same, keep the variable.
  If the digit for the variable in the heading changes, discard the variable.
  We have considered all the variables for the second box, and we are keeping A AND C.
Expression: ¬B V A ∧ B ∧ C |  |  |  |  | 
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C | 0 | 1 |  |  | 1
C | 1 | 1 |  | 1 | 1
A B
C
¬B
Variable A – Keep
Variable B – Discard
Variable C – Keep
A ∧ C

## Slide 73
Using a Karnaugh map to simplify Boolean expressions with three variables
So, the first box represents ¬B.
The second box represents A ∧ C.
The different parts of the expression (the different boxes we are looking at) are separated with OR symbols.
We have simplified the original expression (¬B V A ∧ B ∧ C) to: ¬B V A ∧ C
Expression: ¬B V A ∧ B ∧ C |  |  |  |  | 
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C | 0 | 1 |  |  | 1
C | 1 | 1 |  | 1 | 1
A B
C
¬B
A ∧ C
Simplified expression:
¬B
A ∧ C
V

## Slide 74
Using a Karnaugh map to simplify Boolean expressions with three variables
To recap, when we are considering variables within the same box, if the headings stay the same, we join the variables together with AND (∧).
When we are considering different boxes, we join the expressions together with OR (V).
Expression: ¬B V A ∧ B ∧ C |  |  |  |  | 
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C | 0 | 1 |  |  | 1
C | 1 | 1 |  | 1 | 1
A B
C
¬B
A ∧ C
Simplified expression: ¬B V A ∧ C

## Slide 75
Using a Karnaugh map to simplify Boolean expressions with three variables
Finally, note that the simplified expression ¬B V A ∧ C could also be written as:
  A ∧ C V ¬B
  C ∧ A V ¬B
  ¬B V A ∧ C
  ¬B V C ∧ A
Any of these expressions would be considered correct in the exam.
The different answers come from the order in which you look at the boxes and the variables within them.
Expression: ¬B V A ∧ B ∧ C |  |  |  |  | 
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C | 0 | 1 |  |  | 1
C | 1 | 1 |  | 1 | 1
A B
C
¬B
A ∧ C
Simplified expression: ¬B V A ∧ C

## Slide 76
How can Karnaugh maps be used to simplify Boolean expressions?
Having watched this video, you should be able to answer the following key question.

## Slide 77
SLR15 Boolean algebra
Going beyond the specification

## Slide 78
We mentioned earlier that the headings in Karnaugh maps must use Gray code sequences and not traditional binary sequences.
That means we can only change one bit as we go from one binary number heading to the next – but why?
Gray codes
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C D | 0 0 |  |  |  | 
C D | 0 1 |  |  |  | 
C D | 1 1 |  |  |  | 
C D | 1 0 |  |  |  | 
A B
C D
Gray code sequence

## Slide 79
By using Gray codes, we ensure that adjacent cells will only ever vary by one bit or Boolean variable.
Gray codes are required to organise the outputs of a logic function so we can spot commonality.
Without them, when we place 1s into the map, cells sharing common Boolean variables would no longer be adjacent and would not show visual patterns of commonality.
Gray codes
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C D | 0 0 |  |  |  | 
C D | 0 1 |  |  |  | 
C D | 1 1 |  |  |  | 
C D | 1 0 |  |  |  | 
A B
C D
Gray code sequence

## Slide 80
A Karnaugh map is simply a representation of all the possible states of a truth table for a specified number of variables.
Four variables in a truth table produce 16 possible outputs.
All 16 states are represented on this four-input Karnaugh map.
Using Gray codes, we can transition through the map any way we like and only see single-digit changes.
Remember, we can also move off any edge of the map and re-enter at the opposite edge.
Gray codes
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C D | 0 0 | 0000 | 0100 | 1100 | 1000
C D | 0 1 | 0001 | 0101 | 1101 | 1001
C D | 1 1 | 0011 | 0111 | 1111 | 1011
C D | 1 0 | 0010 | 0110 | 1110 | 1010
A B
C D

## Slide 81
Using a Karnaugh map to simplify Boolean expressions with three variables
If we overlay the Gray codes onto our 2D map and our torus, we can see it still works.
The four corners of a Karnaugh map are next to each other, and as you move from cell to cell, only a single digit changes.
1100
0000
0100
1000
0001
0101
1101
1001
0011
0111
1111
1011
0010
0110
1110
1010
0000
1000
0010
1010
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C D | 0 0 | 0000 | 0100 | 1100 | 1000
C D | 0 1 | 0001 | 0101 | 1101 | 1001
C D | 1 1 | 0011 | 0111 | 1111 | 1011
C D | 1 0 | 0010 | 0110 | 1110 | 1010

## Slide 82
SLR15 Boolean algebra
Boolean Algebra cheat sheet

## Slide 84
student.craigndave.org