## Slide 1
SLR15 Boolean algebra
Karnaugh maps – part 4
Simplifying four-input Karnaugh maps

## Slide 2
A note about this video
This video covers how to simplify four-input Boolean expressions using Karnaugh maps.
It assumes you are already familiar the basics of Karnaugh maps.
If you have not seen them yet, we suggest you go back and watch:
  Karnaugh maps Part 1
  Karnaugh maps Part 2
  Karnaugh maps Part 3

## Slide 3
Karnaugh maps are a method of simplifying Boolean expressions.
A four-input Karnaugh map can be used to illustrate an expression with four variables.
The expression we want to simplify here is: ¬C ∧ D V A ∧ B
Expression: ¬C ∧ D V A ∧ B |  |  |  |  | 
Using a Karnaugh map to simplify Boolean expressions with four variables

## Slide 4
Karnaugh maps are a method of simplifying Boolean expressions.
A four-input Karnaugh map can be used to illustrate an expression with four variables.
The expression we want to simplify here is: ¬C ∧ D V A ∧ B
As we have four variables, we put two across each axis.
In this case, we have decided to put A/B across the top and C/D down the side, but we could have gone with any configuration we like.
Expression: ¬C ∧ D V A ∧ B |  |  |  |  | 
A B
A B
A B
A B
A B
C D
C D
C D
C D
C D
Using a Karnaugh map to simplify Boolean expressions with four variables

## Slide 5
We then insert the binary headings representing all the possible states of each of the four variables.
Remember, the order of the binary numbers in the headings matters – we cannot simply count up in binary.
As we move from one position to the next, we can only change a single digit at a time.
These sequences are known as Gray codes – we explained what they are and the reason we need to use them at the end of the last video.
Expression: ¬C ∧ D V A ∧ B |  |  |  |  | 
 |  | A B | A B | A B | A B
C D |  |  |  |  | 
C D |  |  |  |  | 
C D |  |  |  |  | 
C D |  |  |  |  | 
A B
C D
0 0
0 0
0 1
0 1
1 1
1 1
1 0
1 0
Using a Karnaugh map to simplify Boolean expressions with four variables

## Slide 6
Expression: ¬C ∧ D V A ∧ B |  |  |  |  | 
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C D | 0 0 |  |  |  | 
C D | 0 1 |  |  |  | 
C D | 1 1 |  |  |  | 
C D | 1 0 |  |  |  | 
A B
C D
Now our Karnaugh map is ready, we will place the first part of the expression into it.
Remember, we separate the expressions using OR symbols.
Using a Karnaugh map to simplify Boolean expressions with four variables
¬C ∧ D V A ∧ B
OR
V

## Slide 7
Expression: ¬C ∧ D V A ∧ B |  |  |  |  | 
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C D | 0 0 |  |  |  | 
C D | 0 1 |  |  |  | 
C D | 1 1 |  |  |  | 
C D | 1 0 |  |  |  | 
A B
C D
Now our Karnaugh map is ready, we will place the first part of the expression into it.
Remember, we separate the expressions using OR symbols.
We are starting with NOT C AND D.
There are four cells where C is 0 and D is 1 – we put 1s in these cells.
The expression we are looking at only contains C and D, so we can ignore A and B at this stage.
Using a Karnaugh map to simplify Boolean expressions with four variables
¬C ∧ D V A ∧ B
OR
V
1
1
1
1

## Slide 8
Expression: ¬C ∧ D V A ∧ B |  |  |  |  | 
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C D | 0 0 |  |  |  | 
C D | 0 1 | 1 | 1 | 1 | 1
C D | 1 1 |  |  |  | 
C D | 1 0 |  |  |  | 
A B
C D
We now move onto the next part of the expression: A AND B
To put A AND B in the map, we find all the cells where A is 1 and B is 1.
Using a Karnaugh map to simplify Boolean expressions with four variables
¬C ∧ D V A ∧ B
OR
V

## Slide 9
Expression: ¬C ∧ D V A ∧ B |  |  |  |  | 
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C D | 0 0 |  |  |  | 
C D | 0 1 | 1 | 1 | 1 | 1
C D | 1 1 |  |  |  | 
C D | 1 0 |  |  |  | 
A B
C D
We now move onto the next part of the expression: A AND B
To put A AND B in the map, we find all the cells where A is 1 and B is 1.
There are four cells where this is the case – we put a 1 in each of them.
Using a Karnaugh map to simplify Boolean expressions with four variables
¬C ∧ D V A ∧ B
OR
V
1
1
1

## Slide 10
Expression: ¬C ∧ D V A ∧ B |  |  |  |  | 
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C D | 0 0 |  |  | 1 | 
C D | 0 1 | 1 | 1 | 1 | 1
C D | 1 1 |  |  | 1 | 
C D | 1 0 |  |  | 1 | 
A B
C D
Now we have placed all parts of the expression into the map, we can simplify it by drawing boxes around the 1s, making sure to remember the rules for doing so:
  Boxes must be rectangles or squares.
  No diagonal boxes
  Boxes can only contain 1s.
  Boxes must be as large as possible.
  Boxes of 2n 1s: 1, 2, 4, 8 or 16 digits.
  Boxes can overlap.
  Smallest possible number of boxes.
Using a Karnaugh map to simplify Boolean expressions with four variables

## Slide 11
Expression: ¬C ∧ D V A ∧ B |  |  |  |  | 
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C D | 0 0 |  |  | 1 | 
C D | 0 1 | 1 | 1 | 1 | 1
C D | 1 1 |  |  | 1 | 
C D | 1 0 |  |  | 1 | 
A B
C D
Given all these rules, the most optimal outcome is shown here.
These two boxes will now allow us to simplify the original expression.
Using a Karnaugh map to simplify Boolean expressions with four variables

## Slide 12
Expression: ¬C ∧ D V A ∧ B |  |  |  |  | 
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C D | 0 0 |  |  | 1 | 
C D | 0 1 | 1 | 1 | 1 | 1
C D | 1 1 |  |  | 1 | 
C D | 1 0 |  |  | 1 | 
A B
C D
If we consider the headings for each box and each variable within those boxes, we can see that:
  A stays the same
  B stays the same
  C stays the same
  D stays the same
We have to keep any variables that stay the same – they all stay the same, so we keep all the variables.
That means this expression cannot be simplified.
Using a Karnaugh map to simplify Boolean expressions with four variables

## Slide 13
Expression: ¬A ∧ B ∧ C ∧ D V ¬A ∧ B ∧ C V ¬D |  |  |  |  | 
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C D | 0 0 |  |  |  | 
C D | 0 1 |  |  |  | 
C D | 1 1 |  |  |  | 
C D | 1 0 |  |  |  | 
Using a Karnaugh map to simplify Boolean expressions with four variables
Let’s try another example: ¬A ∧ B ∧ C ∧ D V ¬A ∧ B ∧ C V ¬D
We have set up our blank Karnaugh map already.
As always, we separate the expressions with OR symbols and place the first part into the map.
A B
C D
¬A ∧ B ∧ C ∧ D V ¬A ∧ B ∧ C V ¬D
OR
V
OR
V

## Slide 14
Expression: ¬A ∧ B ∧ C ∧ D V ¬A ∧ B ∧ C V ¬D |  |  |  |  | 
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C D | 0 0 |  |  |  | 
C D | 0 1 |  |  |  | 
C D | 1 1 |  |  |  | 
C D | 1 0 |  |  |  | 
Using a Karnaugh map to simplify Boolean expressions with four variables
We are starting with NOT A AND B AND C AND D.
There is only one cell where A is 0 while B, C and D are 1 – we put a 1 in this cell.
A B
C D
¬A ∧ B ∧ C ∧ D V ¬A ∧ B ∧ C V ¬D
OR
V
OR
V
1

## Slide 15
Expression: ¬A ∧ B ∧ C ∧ D V ¬A ∧ B ∧ C V ¬D |  |  |  |  | 
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C D | 0 0 |  |  |  | 
C D | 0 1 |  |  |  | 
C D | 1 1 |  | 1 |  | 
C D | 1 0 |  |  |  | 
Using a Karnaugh map to simplify Boolean expressions with four variables
We now move onto the next part: NOT A AND B AND C
A B
C D
¬A ∧ B ∧ C ∧ D V ¬A ∧ B ∧ C V ¬D
OR
V
OR
V

## Slide 16
Expression: ¬A ∧ B ∧ C ∧ D V ¬A ∧ B ∧ C V ¬D |  |  |  |  | 
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C D | 0 0 |  |  |  | 
C D | 0 1 |  |  |  | 
C D | 1 1 |  | 1 |  | 
C D | 1 0 |  |  |  | 
Using a Karnaugh map to simplify Boolean expressions with four variables
We now move onto the next part: NOT A AND B AND C
A must be 0 while B and C are 1. There are two cells where this is true – we put a 1 in each of them.
A B
C D
¬A ∧ B ∧ C ∧ D V ¬A ∧ B ∧ C V ¬D
OR
V
OR
V
1

## Slide 17
Expression: ¬A ∧ B ∧ C ∧ D V ¬A ∧ B ∧ C V ¬D |  |  |  |  | 
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C D | 0 0 |  |  |  | 
C D | 0 1 |  |  |  | 
C D | 1 1 |  | 1 |  | 
C D | 1 0 |  | 1 |  | 
Using a Karnaugh map to simplify Boolean expressions with four variables
We now move onto the final part of the expression: NOT D
A B
C D
¬A ∧ B ∧ C ∧ D V ¬A ∧ B ∧ C V ¬D
OR
V
OR
V

## Slide 18
Expression: ¬A ∧ B ∧ C ∧ D V ¬A ∧ B ∧ C V ¬D |  |  |  |  | 
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C D | 0 0 |  |  |  | 
C D | 0 1 |  |  |  | 
C D | 1 1 |  | 1 |  | 
C D | 1 0 |  | 1 |  | 
Using a Karnaugh map to simplify Boolean expressions with four variables
We now move onto the final part of the expression: NOT D
As this part of the expression only contains the variable D, we can ignore C at this stage.
There are eight cells where D is 0 –we put a 1 in each of them.
A B
C D
¬A ∧ B ∧ C ∧ D V ¬A ∧ B ∧ C V ¬D
OR
V
OR
V
1
1
1
1
1
1
1

## Slide 19
Expression: ¬A ∧ B ∧ C ∧ D V ¬A ∧ B ∧ C V ¬D |  |  |  |  | 
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C D | 0 0 | 1 | 1 | 1 | 1
C D | 0 1 |  |  |  | 
C D | 1 1 |  | 1 |  | 
C D | 1 0 | 1 | 1 | 1 | 1
Using a Karnaugh map to simplify Boolean expressions with four variables
Now we have placed all parts of the expression into the map, we can simplify it by drawing boxes around the 1s, making sure to remember the rules for doing so:
  Boxes must be rectangles or squares.
  No diagonal boxes
  Boxes can only contain 1s.
  Boxes must be as large as possible.
  Boxes of 2n 1s: 1, 2, 4, 8 or 16 digits.
  Boxes can overlap.
  Smallest possible number of boxes.
A B
C D

## Slide 20
Expression: ¬A ∧ B ∧ C ∧ D V ¬A ∧ B ∧ C V ¬D |  |  |  |  | 
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C D | 0 0 | 1 | 1 | 1 | 1
C D | 0 1 |  |  |  | 
C D | 1 1 |  | 1 |  | 
C D | 1 0 | 1 | 1 | 1 | 1
Using a Karnaugh map to simplify Boolean expressions with four variables
Given all these rules, the most optimal outcome is shown here.
We have identified one large box of eight using the wrap-around rule…
A B
C D

## Slide 21
Expression: ¬A ∧ B ∧ C ∧ D V ¬A ∧ B ∧ C V ¬D |  |  |  |  | 
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C D | 0 0 | 1 | 1 | 1 | 1
C D | 0 1 |  |  |  | 
C D | 1 1 |  | 1 |  | 
C D | 1 0 | 1 | 1 | 1 | 1
Using a Karnaugh map to simplify Boolean expressions with four variables
Given all these rules, the most optimal outcome is shown here.
We have identified one large box of eight using the wrap-around rule…
…and a second box of two.
These two boxes will now allow us to simplify the original expression.
A B
C D

## Slide 22
Expression: ¬A ∧ B ∧ C ∧ D V ¬A ∧ B ∧ C V ¬D |  |  |  |  | 
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C D | 0 0 | 1 | 1 | 1 | 1
C D | 0 1 |  |  |  | 
C D | 1 1 |  | 1 |  | 
C D | 1 0 | 1 | 1 | 1 | 1
Using a Karnaugh map to simplify Boolean expressions with four variables
How do we determine the simplified expression from these boxes?
  Take each box in any order.
  Take each variable in any order.
  If the digit for the variable in the heading stays the same, keep the variable.
  If the digit for the variable in the heading changes, discard the variable.
A B
C D

## Slide 23
Expression: ¬A ∧ B ∧ C ∧ D V ¬A ∧ B ∧ C V ¬D |  |  |  |  | 
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C D | 0 0 | 1 | 1 | 1 | 1
C D | 0 1 |  |  |  | 
C D | 1 1 |  | 1 |  | 
C D | 1 0 | 1 | 1 | 1 | 1
Using a Karnaugh map to simplify Boolean expressions with four variables
How do we determine the simplified expression from these boxes?
  Take each box in any order.
  Take each variable in any order.
  If the digit for the variable in the heading stays the same, keep the variable.
  If the digit for the variable in the heading changes, discard the variable.
We choose to explore the large box of eight 1s first.
Within that box, we decide to consider variable A first.
The number in the heading for A changes, so we discard it.
A B
C D
A Discard

## Slide 24
Expression: ¬A ∧ B ∧ C ∧ D V ¬A ∧ B ∧ C V ¬D |  |  |  |  | 
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C D | 0 0 | 1 | 1 | 1 | 1
C D | 0 1 |  |  |  | 
C D | 1 1 |  | 1 |  | 
C D | 1 0 | 1 | 1 | 1 | 1
Using a Karnaugh map to simplify Boolean expressions with four variables
How do we determine the simplified expression from these boxes?
  Take each box in any order.
  Take each variable in any order.
  If the digit for the variable in the heading stays the same, keep the variable.
  If the digit for the variable in the heading changes, discard the variable.
We now consider variable B from the same box.
The number in the heading for B changes, so we discard it.
A B
C D
A Discard
B Discard

## Slide 25
Expression: ¬A ∧ B ∧ C ∧ D V ¬A ∧ B ∧ C V ¬D |  |  |  |  | 
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C D | 0 0 | 1 | 1 | 1 | 1
C D | 0 1 |  |  |  | 
C D | 1 1 |  | 1 |  | 
C D | 1 0 | 1 | 1 | 1 | 1
Using a Karnaugh map to simplify Boolean expressions with four variables
How do we determine the simplified expression from these boxes?
  Take each box in any order.
  Take each variable in any order.
  If the digit for the variable in the heading stays the same, keep the variable.
  If the digit for the variable in the heading changes, discard the variable.
We now consider variable C from the same box.
The number in the heading for C changes, so we discard it.
A B
C D
A Discard
B Discard
C Discard

## Slide 26
Expression: ¬A ∧ B ∧ C ∧ D V ¬A ∧ B ∧ C V ¬D |  |  |  |  | 
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C D | 0 0 | 1 | 1 | 1 | 1
C D | 0 1 |  |  |  | 
C D | 1 1 |  | 1 |  | 
C D | 1 0 | 1 | 1 | 1 | 1
Using a Karnaugh map to simplify Boolean expressions with four variables
How do we determine the simplified expression from these boxes?
  Take each box in any order.
  Take each variable in any order.
  If the digit for the variable in the heading stays the same, keep the variable.
  If the digit for the variable in the heading changes, discard the variable.
Finally, we consider variable D from the same box.
The number in the heading for D stays the same, so we can keep it.
Remember, as the number is a zero, we are keeping NOT D (¬D).
A B
C D
A Discard
B Discard
C Discard
¬D Keep

## Slide 27
Expression: ¬A ∧ B ∧ C ∧ D V ¬A ∧ B ∧ C V ¬D |  |  |  |  | 
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C D | 0 0 | 1 | 1 | 1 | 1
C D | 0 1 |  |  |  | 
C D | 1 1 |  | 1 |  | 
C D | 1 0 | 1 | 1 | 1 | 1
Using a Karnaugh map to simplify Boolean expressions with four variables
We are finished with the large box of eight 1s, and the only variable we are keeping is ¬D.
We now know this entire box can be simplified down to: ¬D
A B
C D
A Discard
B Discard
C Discard
¬D Keep
¬D

## Slide 28
Expression: ¬A ∧ B ∧ C ∧ D V ¬A ∧ B ∧ C V ¬D |  |  |  |  | 
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C D | 0 0 | 1 | 1 | 1 | 1
C D | 0 1 |  |  |  | 
C D | 1 1 |  | 1 |  | 
C D | 1 0 | 1 | 1 | 1 | 1
Using a Karnaugh map to simplify Boolean expressions with four variables
How do we determine the simplified expression from these boxes?
  Take each box in any order.
  Take each variable in any order.
  If the digit for the variable in the heading stays the same, keep the variable.
  If the digit for the variable in the heading changes, discard the variable.
We now move onto the other box, which contains two 1s, and we decide to consider A first.
The number in the heading for A stays the same as there is only one instance of it, so we keep it.
Remember, as the number is a zero, we are keeping NOT A (¬A).
A B
C D
¬A Keep
¬D

## Slide 29
Expression: ¬A ∧ B ∧ C ∧ D V ¬A ∧ B ∧ C V ¬D |  |  |  |  | 
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C D | 0 0 | 1 | 1 | 1 | 1
C D | 0 1 |  |  |  | 
C D | 1 1 |  | 1 |  | 
C D | 1 0 | 1 | 1 | 1 | 1
Using a Karnaugh map to simplify Boolean expressions with four variables
How do we determine the simplified expression from these boxes?
  Take each box in any order.
  Take each variable in any order.
  If the digit for the variable in the heading stays the same, keep the variable.
  If the digit for the variable in the heading changes, discard the variable.
We now move onto variable B.
The number in the heading for B stays the same, as there is only one instance of it, so we keep it.
A B
C D
¬A Keep
B Keep
¬D

## Slide 30
Expression: ¬A ∧ B ∧ C ∧ D V ¬A ∧ B ∧ C V ¬D |  |  |  |  | 
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C D | 0 0 | 1 | 1 | 1 | 1
C D | 0 1 |  |  |  | 
C D | 1 1 |  | 1 |  | 
C D | 1 0 | 1 | 1 | 1 | 1
Using a Karnaugh map to simplify Boolean expressions with four variables
How do we determine the simplified expression from these boxes?
  Take each box in any order.
  Take each variable in any order.
  If the digit for the variable in the heading stays the same, keep the variable.
  If the digit for the variable in the heading changes, discard the variable.
We now move onto variable C.
The number in the heading for C stays the same, so we keep it.
A B
C D
¬A Keep
B Keep
C Keep
¬D

## Slide 31
Expression: ¬A ∧ B ∧ C ∧ D V ¬A ∧ B ∧ C V ¬D |  |  |  |  | 
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C D | 0 0 | 1 | 1 | 1 | 1
C D | 0 1 |  |  |  | 
C D | 1 1 |  | 1 |  | 
C D | 1 0 | 1 | 1 | 1 | 1
Using a Karnaugh map to simplify Boolean expressions with four variables
How do we determine the simplified expression from these boxes?
  Take each box in any order.
  Take each variable in any order.
  If the digit for the variable in the heading stays the same, keep the variable.
  If the digit for the variable in the heading changes, discard the variable.
We now move onto variable D.
The number in the heading for D changes, so we discard it.
A B
C D
¬D
¬A Keep
B Keep
C Keep
D Discard

## Slide 32
Expression: ¬A ∧ B ∧ C ∧ D V ¬A ∧ B ∧ C V ¬D |  |  |  |  | 
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C D | 0 0 | 1 | 1 | 1 | 1
C D | 0 1 |  |  |  | 
C D | 1 1 |  | 1 |  | 
C D | 1 0 | 1 | 1 | 1 | 1
Using a Karnaugh map to simplify Boolean expressions with four variables
We are now finished with the second box, and we are keeping NOT A, B and C.
We join any terms that we are keeping from within a single box with ANDs (∧).
So, we now know this box can be simplified to: ¬A ∧ B ∧ C
A B
C D
¬D
¬A Keep
B Keep
C Keep
D Discard
¬A ∧ B ∧ C

## Slide 33
Expression: ¬A ∧ B ∧ C ∧ D V ¬A ∧ B ∧ C V ¬D |  |  |  |  | 
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C D | 0 0 | 1 | 1 | 1 | 1
C D | 0 1 |  |  |  | 
C D | 1 1 |  | 1 |  | 
C D | 1 0 | 1 | 1 | 1 | 1
Using a Karnaugh map to simplify Boolean expressions with four variables
The first box represents: ¬D
The second box represents: ¬A ∧ B ∧ C
Different parts of the expression (the different boxes we are looking at) are separated using ORs.
So, we have simplified the original expression (¬A ∧ B ∧ C ∧ D V ¬A ∧ B ∧ C V ¬D) to: ¬D V ¬A ∧ B ∧ C
A B
C D
Simplified expression:
V
¬D
¬A ∧ B ∧ C

## Slide 34
Expression: ¬A ∧ B ∧ C ∧ D V ¬A ∧ B ∧ C V ¬D Simplified expression: ¬D V ¬A ∧ B ∧ C |  |  |  |  | 
 |  | A B | A B | A B | A B
 |  | 0 0 | 0 1 | 1 1 | 1 0
C D | 0 0 | 1 | 1 | 1 | 1
C D | 0 1 |  |  |  | 
C D | 1 1 |  | 1 |  | 
C D | 1 0 | 1 | 1 | 1 | 1
Using a Karnaugh map to simplify Boolean expressions with four variables
This simplified expression could also be written as ¬A ∧ B ∧ C V ¬D, and there are many other valid combinations.
The order of your simplified expression is determined only by the order in which you consider the boxes and variables.
However, because of the law of commutation, each version is valid and will be accepted in the exam.
A B
C D

## Slide 35
How can Karnaugh maps be used to simplify Boolean expressions?
Having watched this video, you should be able to answer the following key question.

## Slide 36
SLR15 Boolean algebra
Boolean Algebra cheat sheet

## Slide 38
student.craigndave.org