## Slide 1: LANS and WANS
A Level Computer Science – Unit 1

## Slide 2: WAN – Wide Area Networks
As a network of inter-connected networks, the Internet comprises millions, if not billions of Local Area Networks and individual users to form the world 's largest Wide Area Network. The Internet is the largest and most famous Wide Area Network in the world. But some large and medium-sized organisations have their own private Wide Area Networks, or WANs.
A WAN is a collection of computers and networks connected together using resources supplied by a “third party carrier” such as British Telecom.

## Slide 3: WAN – Wide Area Networks
It uses cables, telephone lines, satellites and radio waves to connect the components, which are usually spread over a wide geographical area.
A business with offices in London, Leeds, Bristol and York may lease connections from a network service provider to connect the four office LANs together.

## Slide 4: LAN – Local Area Networks
A Local Area Network (LAN) usually covers a relatively small geographical area. It consists of a collection of computers and peripheral devices (such as printers) connected together, often on a single site. In some schools they have many different buildings, the school’s LAN connects the computers in all of these buildings. A LAN is often owned and managed by a single person or organisation.

## Slide 5: Benefits of networking computers
These are some of the benefits of networking computers belonging to a single organisation.
Sharing resources
Folders and files can be stored on a file server so they can be accessed from any computer on the network
Peripheral devices such as printers can be shared
Internet connection can be shared and any authorisation user on the network can use email.

## Slide 6: Benefits of networking computers
Centralised management
User profiles and security can be managed centrally
Software can be shared across the network rather than having to install on every computer
All files can be backed up centrally

## Slide 7: Disadvantages of networking computers
The disadvantages of networking computers include administration and security:
Managing a large network is complicated
Viruses may be able to infiltrate the network and infect every computer

## Slide 8: Physical bus topology
A LAN can use different layouts or topologies. In a bus topology, all computers are connected to a single cable. The ends of the cable are plugged into a terminator.

## Slide 9: Physical bus topology
Advantage of a bus topology
Inexpensive to install as it requires less cable than a star topology and does not require any additional hardware
Disadvantages of a bus topology
If the main cable fails, network data can no longer be transmitted to any of the nodes
Performance degrades with heavy traffic
Low security - all computers on the network can see all data transmissions

## Slide 10: Physical star topology
A star network has a central node, which may be a switch or computer which acts as a router to transmit messages. A switch keeps a record of the unique MAC address of each device on the network and can identify which particular computer on the network it should send the data to.

## Slide 11: Advantages of a star topology
If one cable fails, only one station is affected, so it is simple to isolate faults
Consistent performance even when the network is being heavily used
Higher transmission speeds can give better performance than a bus network
No problems with 'collisions' of data since each station has its own cable to the server
The system is more secure as messages are sent directly to the central computer and cannot be intercepted by other stations
Easy to add new stations without disrupting the network

## Slide 12: Disadvantages of a star network
May be costly to install because of the length of cable required
If the central device goes down, network data can no longer be transmitted to any of the nodes

## Slide 13: Physical vs logical topology
The physical topology of a network is its actual design layout, which is important when you select a wiring scheme and design the wiring for a new network.
The logical topology is the shape of the path the data travels in, and describes how components communicate across the physical topology. The physical and logical topologies are independent of other, so that a network physically wired in star topology can behave logically as a bus network by a bus protocol and appropriate physical switching.

## Slide 14: Physical vs logical topology
For example, any variety of Ethernet uses a logical bus topology when components communicate, regardless of the physical layout of the cable.

## Slide 15: Wi-Fi
Wi-Fi is a local area wireless technology that enables you to connect a device such as a PC, smartphone, digital audio player, laptop or tablet computer to a network resource or to the Internet via a wireless network access point (WAP). An access point has a range of about 20 metres indoors, and more outdoors.

## Slide 16: Wi-Fi
In 1999, the Wi-Fi Alliance was formed to establish international standards for interoperability and backward compatibility. The Alliance consists of a group of several hundred companies around the and enforces the use of standards for device connectivity and network connections.

## Slide 17: Wireless Access Point (WAP)
In order to connect to a wireless network, a computer device needs a wireless network adaptor.
The combination of computer and interface controller is called a station . All stations share a single radio frequency communication channel, and each station is constantly tuned in on this frequency to pick up transmissions. Transmissions are received by all the stations within range of the wireless access point.

## Slide 18: Wireless Access Point (WAP)
To connect to the Internet, the WAP usually connects to a router, but it can also be an integral part of the router itself.

## Slide 19: Mesh network topologies
Mesh networks are becoming more common with the widespread use of wireless technology. Each node in a mesh network has a connection to every other node, by transmitting data across any intermediate nodes. Only one node requires a connection to the Internet and all others can share this connection. Mesh networks can quickly become big enough to cover entire cities.

## Slide 20: Advantages of a wireless mesh network
The advantages of a mesh network include:
No cabling costs
The more nodes that are installed, the faster and more reliable the network becomes, since one blocked or broken connection (as shown above) can easily be circumvented by another route. In this respect, the mesh topology can be described as 'self healing'.
New nodes are automatically incorporated into the network
Faster communication since data packets do not need to travel via a central switch.