## Slide 1: Packet and Circuit Switching
A Level Computer Science – Unit 1

## Slide 2: Circuit switching
Circuit switching creates a direct link between two devices for the duration of the communication.
The public telephone system is an example of a circuit switched network. When a caller dials a number, various switches in telephone exchanges set up a path between the caller and the recipient.
The connection is set up for the entire duration of the call including periods of silence and pauses. This enables two people to hold a call without any delay in the delivery of speech.

## Slide 3: Circuit switching
If two computers use the circuit switching principle, bandwidth is wasted during the periods when no data is being sent. The two devices must also transmit and receive data at the same rate, so circuit switched networks can only connect computers or devices that operate at the same transfer rate.
On the other hand, since this is an exclusive connection between the two devices for the duration of the communication, data segments (or packets) arrive in the same order that they are sent, simplifying the process of reconstructing the message at the recipient end

## Slide 4: Circuit switching
Because switches are used to connect and disconnect the circuits, electrical interference is produced and although this is not a serious problem for speech, it may produce corrupt or lost data if the path is being used to transmit data. If this is likely to be a problem, a leased line may be used instead.

## Slide 5: Packet switching
Packet switching is a method of communicating packets of data across a network on which other similar communications are happening simultaneously. Website data that you receive arrives as a series of packets and an email will leave you in a series of packets.

## Slide 6: Data packets
Data that is to be transmitted across a network is broken down into more manageable chunks called packets . The size of each packet in a transmission can be fixed or variable, but most are between 500 and 1500 bytes. Each packet contains a header and a payload containing the body of data being sent.
Some packets may also use a trailer section with a checksum or Cyclical Redundancy Check (CRC) to detect transmission errors by creating and attaching a hash total calculated from the data contained in the packets.

## Slide 7: Data packets
In essence, this hash total commonly involves adding up the total number of 1 s in the transmission. The CRC checksum is recalculated for each packet upon receipt and matched to help verify that the payload data has not changed during transmission, If the CRC totals differ, the packet is refused with suspected data corruption and a new copy is requested from the sender.

## Slide 8: Data packets
The header (much like the box(es) of a consignment you might send or receive through the post) includes
the sender's and the recipient's IP addresses, the protocol being used with this type of packet and the number of the packet in the sequence being sent, e.g. packet 1 of 8. They also include the Time To Live (TTL) or hop limit, after which point the data packet expires and is discarded.
The payload of the packet contains the actual data being sent. Upon receipt, the packets are reassembled in the correct order and the data is extracted.

## Slide 9: Routing packets across the Internet
The success of packet switching relies on the ability of packets to be sent from sender to recipient along entirely separate routes from each other. At the moment that a packet leaves the sender's computer, the fastest or least congested route is taken to the recipient's computer. They can be easily reassembled in the correct order at the receiving end and any packets that don't make it can be requested again.

## Slide 10: Routers
Each node in the diagram above represents a router. Routers are used to connect at least two networks, commonly two LANs or WANs, or to connect a LAN and its ISP's network.
The act of traversing between one router and another across a network is referred to as a hop. The job of a router is to read the recipient's IP address in each packet and forward it on to the recipient via the fastest and least congested route to the next router, which will do the same until the packet reaches its destination. Routers use routing tables to store and update the locations of other network devices and the most efficient routes to them. A routing algorithm is used to find the optimum route.

## Slide 11: Routers
The routing algorithm used to decide the best route can become a bottleneck in network traffic since the decision making process can be complicated. A common shortest path algorithm used in routing is Dijkstra's algorithm. When a router is connected to the Internet, the IP address of the port connecting it must be registered with the Internet registry because this IP address must be unique over the whole Internet.

## Slide 12: Gateways
Routing packets from one network to another requires a router if the networks share the same protocols, for example TCP/IP. Where these protocols differ between networks, a gateway is used rather than a router to translate between them.

## Slide 13: Gateways
All of the header data is stripped from the packet leaving only the raw data and new data is added in the format of the new network before the gateway sends the packet on its way again. Gateways otherwise perform a similar job to routers in moving data packets towards their destination.

## Slide 14: Media Access Control (MAC) addresses
Every computer device, whether it's a PC, smartphone, laptop, printer or other device which is capable of being part of a network, must have a wired or wireless Network Interface Card (NIC).
Each NIC has a unique Media Access Control address (MAC address), which is assigned and hard-coded into the card by the manufacturer and which uniquely identifies the device. The address is 48 bits long, and is written as 12 hex digits, for example:
00-09-S0-E3-F7 -62

## Slide 15: Media Access Control (MAC) addresses
You can find out the MAC address of your PC by selecting Command Prompt from the Start menu in Windows, and then typing ipconfig /all. This will display the physical address, i.e. MAC address.