## Slide 1: Addition, Subtraction of Binary
Data Types

## Slide 2: Binary addition
Binary addition works in a similar way to denary addition. If two numbers added together are equal to or greater than the base value, (in the case of denary, 10) then the 'tens' are carried. In binary, an addition that equals 2 or more results in a carry over to the next column.
In binary, the rules for addition are as follows:
1. 0+0 =0
2. 0 + 1 = 1
3. 1 + 0 = 1
4. 1 + 1 = 0 Carry 1 (This is 2 in denary or 10 in binary.)
5. 1 + 1 + 1 = 1 Carry 1 (This is 3 in denary or 11 in binary.)

## Slide 3: Binary addition
Use the following worked example as a guide to where and how each of the rules is implemented.

## Slide 4: Overflow
In the following example, 8 bits are used to store the result of an addition. This result of the addition is greater than 255, and overflow error occurs where a carry from the most significant bit requires a ninth bit.

## Slide 5: Binary subtraction using two's complement
Binary subtraction is best done by using the negative two's complement number and then adding the second number. For example denary 17-14 would be:
The carry on the addition is ignored, and the correct answer is given.
14 | = | 00001110
-14 | = | 11110010
17 | = | 00010001
17 + (-14) | = | (1) 00000011

## Slide 6: Binary subtraction using two's complement
Binary subtraction is best done by using the negative two's complement number and then adding the second number. For example denary 17-14 would be:
The carry on the addition is ignored, and the correct answer is given.
14 | = | 00001110
-14 | = | 11110010
17 | = | 00010001
17 + (-14) | = | (1) 00000011

## Slide 7: Binary subtraction using two's complement
Convert the following pairs of denary numbers to binary and subtract the second number from the first:
14 and 27
14 and 8

## Slide 8: Binary subtraction using two's complement
(i) 14 = 00001110
27 = 00011011
11100100 flip the bits
-27 = 11100101
14 = 00001110
Sum = 11110011

## Slide 9: Binary subtraction using two's complement
(ii) 8 = 00001000
11110111 flip the bits
1 add 1
-8 = 11111000
14 = 00001110
14-8 = 00000110 = 6 (ignoring the carry)