## Slide 1: Fixed Point Binary
Fixed Point Binary

## Slide 2: Fixed point binary numbers
Fixed point binary numbers can be a useful way to represent fractions in binary. A binary point is used to separate the whole place values from the fractional part on the number line:
In the binary example above, the left hand section before the point is equal to 5 (4+ 1) and the right hand section is equal to 1/2 + 1/4 3/4), or 0.5 + 0.25 = 0.75. So, using four bits after the point, 0101 1100 is 5.75 in denary. A useful table with some denary fractions and their equivalents is given below:

## Slide 3: Fixed point binary numbers

## Slide 4: Converting a denary fraction to fixed point binary
To convert the fractional part of a denary number to binary, you can employ the same technique as you would when converting any denary number to binary. Take the value and subtract each point value from the amount until you are left with O. Take the example 3.5625 using 4 bits to the right of the binary point:
Subtract 0.5: 0.5625 - 0.5 = 0.0625 1
Subtract 0.25 from 0.0625: Won't go 0
Subtract 0.125 from 0.0625: Won't go 0
Subtract 0.0625 from 0.0625: 0.0625 - 0.0625 = 0 1
3 = 0011 in binary. 0.5625 = 1001. So 3.5625 = 00111001

## Slide 5: Converting a denary fraction to fixed point binary
It is worth noticing that this system is not only less accurate than the denary system, but some fractions cannot be represented at all. 0.2, 0.3 and 0.4, for example, will require an infinite number of bits to the right of the point.
The number of fractional places would therefore be truncated and the number will not be accurately stored, causing rounding errors. In our denary system, two denary places can hold all values between .00 and .99. With the fixed point binary system, 2 digits after the point can only represent 0, 1/4, 1/2, or 3/4 and nothing in between.

## Slide 6: Converting a denary fraction to fixed point binary
The range of a fixed point binary number is also limited by the fractional part. For example, if you have only 8 bits to store a number to 2 binary places, you would need 2 digits after the point, leaving only 6 bits before it. 6 bits only gives a range of 0-63. Moving the point one to the left to improve accuracy within the fractional part only serves to half the range to just 0-31.

## Slide 7: Converting a denary fraction to fixed point binary
Even with 32 bits used for each number, including 8 bits for the fractional part after the point, the maximum value that can be stored is only about 8 million. Another format called floating point binary can hold much larger numbers, with greater accuracy.
Floating point form is covered in the next PowerPoint.