## Slide 1: Logic Gates and Truth Tables
Data Structures

## Slide 2: Binary logic
At the most elementary level, an electronic device can only recognise the presence or absence of current or voltage. Either electricity is present or it isn't. This is a switch - on or off, true or false, 1 or O.
With a computer's semiconductor, the voltage at the input and output terminals is measured and is either high or low; 1 or O. Computers comprise billions of these switches and manipulating these sequences of ONs and OFFs can change individual bits.

## Slide 3: Binary logic
Electronic logic gates can take one or more inputs and produce a single output. This output can become the input to another gate and a complicated cascaded sequence of logic gates can be implemented to form a circuit in, for example, the CPU.

## Slide 4: Simple logic gates and truth tables
There are a number of different logic gates that are each designed to perform a different operation in terms of output. We will look at NOT, AND, OR and XOR gates.
Each of these gates may be represented by a truth table showing the output for each possible input or combination of inputs. The four gates are shown over the next few slides. Inputs are usually given algebraic letters such as A, B and C and output is usually represented by P or Q.

## Slide 5: NOT gate (negation)
The NOT gate is represented by the symbol below and inverts the input. The small circle denotes an inverted input.
Using 1 s and Os as inputs to a gate, its operation can summarised in the form of a truth table.
The Boolean algebraic expression is written: Q =  A where  represents NOT.
Input A | Output Q
0 | 1
1 | 0

## Slide 6: AND gate (conjunction)
The Boolean expression for AND is written: Q = A  B where  represents AND.
The truth table reflects the fundamental property of the AND gate: the output of A AND B is 1 only if input A and input B are both 1 .
Input A | Input B | Output Q
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 7: OR gate (disjunction)
The Boolean expression for OR is written: Q = A  B where  represents OR.
Input A | Input B | Output Q
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1

## Slide 8: XOR gate (exclusive disjunction)
The XOR (pronounced ex-or) gate stands for exclusive OR, meaning that the output will be true if one or other input is true, but not both. Compare this to the OR gate, which will accept two true inputs as true also.
The Boolean algebraic expression is written: Q = A ⊻ B where the ⊻ represents XOR, and is the equivalent of Q = (AB)(AB) . This gate is similar to the OR gate but excludes the condition where A and B are both true. XOR is referred to as exclusive OR, and OR is sometimes referred to as inclusive OR.
Input A | Input B | Output Q
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 9: Creating logic gate circuits
Multiple logic gates can be connected to produce an output based on multiple inputs.
This circuit can be represented by the expression
Q =  A  (B  C) or alternatively as
Q = (NOT A) OR (B AND C)

## Slide 10: Creating logic gate circuits
The equivalent truth table is shown below:

## Slide 11: Challenge 1
Draw a truth table for the following circuit::

## Slide 12: Challenge 1
Draw a truth table for the following circuit::
Input A | Input B | Input C | D = B  C | E = A  D | Q =  E
0 | 0 | 0 | 0 | 0 | 1
0 | 0 | 1 | 1 | 0 | 1
0 | 1 | 0 | 1 | 0 | 1
0 | 1 | 1 | 1 | 0 | 1
1 | 0 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 1 | 0
1 | 1 | 0 | 1 | 1 | 0
1 | 1 | 1 | 1 | 1 | 0

## Slide 13: Challenge 2
Show, by drawing a truth table for
P = (AB)  (AB), that P = Q, where Q = AB.

## Slide 14: Challenge 2
Show, by drawing a truth table for
P = (AB)  (AB), that P = Q, where Q = AB.
Input A | Input B |  B | C = A  ( B) | D =( A)  B | P = C  D | Q = A ⊻ B
0 | 0 | 1 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 1 | 1 | 1
1 | 0 | 1 | 1 | 0 | 1 | 1
1 | 1 | 0 | 0 | 0 | 0 | 0

## Slide 15: Challenge 3
Write the Boolean expression Q = ((A ⊻ B) C) using AND, OR, NOT, XOR instead of symbols.
Draw the corresponding logic circuit.

## Slide 16: Challenge 3
NOT ((A XOR B) AND C)
Point out to students that when drawing these circuits, you need to draw the gates in the innermost brackets first, (A XOR B in this case), then combine these with any other expressions (e.g. C) in the next set of brackets, and finally draw the outermost NOT

## Slide 17: Challenge 4
Write the Boolean expression represented by the logic diagram below, using AND, OR and NOT instead of symbols. Then write the same expression using symbols.
What is the output if A, B and C are all True?

## Slide 18: Challenge 4
What is the output if A, B and C are all True?
First write (A AND B). Then write (B AND NOT C) These are the inputs to the OR gate so the expression is P = (A AND B) OR (B AND NOT C)
i.e. P = (A  B)  (B   C)

## Slide 19: Defining problems using Boolean logic
We can define problems in terms of Boolean logic.
Example 1
A boiler has two sensors, a pressure sensor and a temperature sensor. If either the temperature (T) or the
pressure (P) is too high, a valve (V) will close.
This can be expressed as V = T  P or alternatively as V = T OR P

## Slide 20: Defining problems using Boolean logic
The table representing these conditions could be drawn as follows:

## Slide 21: Defining problems using Boolean logic
Example 2
A chemical process has a sensor to detect a dangerous situation, in which case it sounds an alarm (A).
The alarm is sounded if:
either temperature >= 100C AND rotator is OFF
or PH > 6 AND temperature < 100C

## Slide 22: Defining problems using Boolean logic
either temperature >= 100C AND rotator is OFF
or PH > 6 AND temperature < 100C
A table can be drawn to represent these conditions as Boolean values.

## Slide 23: Defining problems using Boolean logic
The conditions can be written as
A = (TR)  (PT) or alternatively as
A = (T AND NOT R) OR (P AND NOT T)
Now the logic circuit for this process can be drawn as follows:

## Slide 24: Challenge 5
Draw the truth table for this alarm system.

## Slide 25: Challenge 5
Draw the truth table for this alarm system.
Input R | Input T | Input P | X = T   R | Y = P   T | A = X  Y
0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 1
0 | 1 | 0 | 1 | 0 | 1
0 | 1 | 1 | 1 | 0 | 1
1 | 0 | 0 | 0 | 0 | 0
1 | 0 | 1 | 0 | 1 | 1
1 | 1 | 0 | 0 | 0 | 0
1 | 1 | 1 | 0 | 0 | 0