## Slide 1: Simplify Boolean
Data Structures

## Slide 2: de Morgan's laws
Augustus de Morgan (1806-1871) was a Cambridge Mathematics professor who formulated two theorems or laws relating to logic. These laws can be used to manipulate and simplify Boolean expressions. Although his theoretical work had little practical application in his lifetime, it became of major significance in the next century in the field of digital electronics, in which TRUE and FALSE can be replaced by ON and OFF or the binary numbers 0 and 1.
Using de Morgan's laws, any Boolean function can be converted to one which uses only NAND functions or only NOR functions, and these can be further converted to an expression using all NAND functions or all NOR functions.
Thus, any integrated circuit can be built from just one type of logic gate. This is an advantage in manufacturing where costs can be kept down by using only one type of gate.

## Slide 3: de Morgan's first law
(A  B) = A B
The truth of this is clear from the Venn diagram on the right. Suppose we have a variable X defined by
x = (A  B)
The truth of this is clear from the Venn diagram on the right. Suppose we have a variable X defined by
x = (A  B)

## Slide 4: de Morgan's first law
Looking at the Venn diagram, A v B is represented by the white area. Since X is not in A v B, it consists of all the grey area. This can be defined as
everything not in A and not in B, i. e.
x = A B

## Slide 5: Challenge 1
Complete the following truth table to show that
(A v B) =  A  B

## Slide 6: Challenge 1
Complete the following truth table to show that
(A v B) =  A  B
A | B | A | B | A  B | (A  B) | A  B
0 | 0 | 1 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 1 | 0 | 0
1 | 0 | 0 | 1 | 1 | 0 | 0
1 | 1 | 0 | 0 | 1 | 0 | 0

## Slide 7: de Morgan's second law
(A  B) = A  B
Again, looking at the Venn diagram on the right, if
X = (A  B)
X cannot be in the white area, so must be in the red, orange, or grey
areas .. That is, X is either not in A, or not in B, or not in either. This is the definition of
X = A B

## Slide 8: Challenge 2
Complete the following truth table to show that
(A  B) = A B

## Slide 9: Challenge 2
Complete the following truth table to show that
(A  B) = A B
A | B | A | B | A  B | (A  B) | A  B
0 | 0 | 1 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 1 | 1 | 1
1 | 0 | 0 | 1 | 1 | 1 | 1
1 | 1 | 0 | 0 | 1 | 0 | 0

## Slide 10: de Morgan’s laws
To Implement each of de Morgan's laws, foliow the three steps:
Complement both terms in the expression, e.g. A, B
Change AND to OR and OR to AND
Invert the result

## Slide 11: Rules of Boolean algebra
In addition to de Morgan 's laws, there are several identities or "rules" which will help you to simplify
Boolean expressions. The most useful are listed to the right.

## Slide 12: Rules of Boolean algebra
In addition to de Morgan 's laws, there are several identities or "rules" which will help you to simplify
Boolean expressions. The most useful are listed to the right.

## Slide 13: Example 1
Use de Morgan's laws and the laws of Boolean algebra to simplify the following Boolean expression:

## Slide 14: Example 2
Use de Morgan's laws to simplify A  B  A  B

## Slide 15: Challenge 3
Use de Morgan's laws to simplify A B (A  B)

## Slide 16: Challenge 3
Use de Morgan's laws to simplify A B (A  B)
A  B  (A  B)
= A  B  (A  B) de Morgan’s law
= A  (A  B)  B commutative law = A  B absorption law
Therefore A  B  (A  B) = A  B

## Slide 17: Example 3

## Slide 18: Challenge 4
Draw a truth table to show that
(A  B)  (A  C) = A  B  C

## Slide 19: Challenge 4
Draw a truth table to show that
(A  B)  (A  C) = A  B  C
A | B | C | A  B | A  C | B  C | (A  B)  (A  C) | A  B  C
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
1 | 1 | 0 | 1 | 1 | 0 | 1 | 1
1 | 0 | 1 | 1 | 1 | 0 | 1 | 1
1 | 0 | 0 | 1 | 1 | 0 | 1 | 1
0 | 1 | 1 | 1 | 1 | 1 | 1 | 1
0 | 1 | 0 | 1 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0

## Slide 20: Example 4
A single output Q is produced from three inputs X,Y and Z. Q is 1only if X and Y are 1, or Z is 1 and Y is 0.
Write the Boolean expression to represent this circuit.

## Slide 21: Example 4
A single output Q is produced from three inputs X,Y and Z. Q is 1only if X and Y are 1, or Z is 1 and Y is 0.
Write the Boolean expression to represent this circuit.
Answer: There are two separate logic gates involved here: X  Y, Z   Y.
The output from these two gates are input to an OR gate.
Q = (X  Y)  (Z Y)
Represent this equation diagrammatically using a combination of AND, OR and NOT gates.

## Slide 22: Example 4
Answer: There are two separate logic gates involved here: X  Y, Z   Y.
The output from these two gates are input to an OR gate.
Q = (X  Y)  (Z Y)
Represent this equation diagrammatically using a combination of AND, OR and NOT gates.
Answer

## Slide 23: Example 5
Write the Boolean expression corresponding t~ the following logic circuit.
Answer: A  (B  C)