## Slide 1
Association
Boolean algebra
Association allows for the removal of brackets from an expression if all the operators are the same.
Using logic gates, draw the following expression: A V (B V C) . Complete the truth table for the expression.
A | B | C | B V C | A V (B V C)
0 | 0 | 0 |  | 
0 | 0 | 1 |  | 
0 | 1 | 0 |  | 
0 | 1 | 1 |  | 
1 | 0 | 0 |  | 
1 | 0 | 1 |  | 
1 | 1 | 0 |  | 
1 | 1 | 1 |  | 

## Slide 2
Association
Boolean algebra
Complete the truth table for the expression: A V B V C.
A
B
A | B | C | A V B V C
0 | 0 | 0 | 
0 | 0 | 1 | 
0 | 1 | 0 | 
0 | 1 | 1 | 
1 | 0 | 0 | 
1 | 0 | 1 | 
1 | 1 | 0 | 
1 | 1 | 1 | 
The two truth tables deliver the same output. Therefore the two circuit diagrams are equivalent to each other.
The second circuit uses less components so it is preferable. This is an illustration of simplifying a Boolean expression using the association rule.
C

## Slide 3
Association
Boolean algebra
Using the association rule, simplify the following expressions:
X V (Y V Z) V W ≡
(X Ʌ Y) Ʌ (W Ʌ Z) ≡
(A V ¬B) V ¬ A ≡