## Slide 1
Use the following rules to derive or simplify statements in Boolean algebra: De Morgan's Laws, distribution, association, commutation, double negation
Boolean algebra
There is no algorithm as to which rule should be applied when to simplify an expression.
To make simplification a little easier attempt these goals when solving problems:
  Remove brackets where possible. Look for opportunities to apply association, De Morgan’s law and double negation to do this.
  Remove duplicate inputs. E.g. A V A ≡ A and ¬A V ¬A ≡ ¬A
  Remember ¬A Ʌ A = 0 and ¬A V A = 1. This allows you to remove an input and replace it with a value.
  Any expression AND 0 will always be 0, so the expression can be removed.
  Attempt to use distribution to remove one term. E.g. (A Ʌ B) V (A Ʌ C) ≡ A Ʌ (B V C) (A V B) Ʌ (A V C) ≡ A V (B Ʌ C)

## Slide 2
Use the following rules to derive or simplify statements in Boolean algebra: De Morgan's Laws, distribution, association, commutation, double negation
Boolean algebra
When simplifying expressions, sometimes it is necessary to initially expand an expression in order to simplify it in a subsequent step.
¬(A Ʌ B) Ʌ A
Can be expanded to: (¬A V ¬B) Ʌ A
Can be expanded to: (¬A Ʌ A ) V (¬B Ʌ A)
A general rule can now be appled to eliminate (¬A Ʌ A )
Another example with OR:
¬(A Ʌ B) V A
Can be expanded to: (¬A V ¬B) V A Can be expanded to: (¬A V A) V (¬B V A)
A general rule can now be applied to eliminate (¬A V A)

## Slide 3
Use the following rules to derive or simplify statements in Boolean algebra: De Morgan's Laws, distribution, association, commutation, double negation
Boolean algebra
Simplify the expressions:
A Ʌ A V B ≡
B Ʌ (A V ¬A) ≡
(X Ʌ Y) V (X Ʌ Z) ≡
(A V B) Ʌ (A V ¬B) ≡
(X Ʌ Z) V W V (X Ʌ Y) ≡
(A Ʌ B) V A Ʌ (B V C) ≡
¬A V C V (A Ʌ B) ≡

## Slide 4
Use the following rules to derive or simplify statements in Boolean algebra: De Morgan's Laws, distribution, association, commutation, double negation
Boolean algebra
Complete the truth table to show that F V ¬F V ¬G is True, and therefore F V ¬(F Ʌ G) is also True.
F | G | ¬F | ¬G | F V ¬F V ¬G
Simplify the expressions:
¬(X Ʌ Y) Ʌ X ≡
¬(A Ʌ B) V A ≡
(F Ʌ ¬G) V G ≡

## Slide 5
Use the following rules to derive or simplify statements in Boolean algebra: De Morgan's Laws, distribution, association, commutation, double negation
Boolean algebra
Simplify the expressions:
¬X V ¬Y V X Ʌ Y ≡
¬(X Ʌ Y) V ¬Y V X ≡
A V B V ¬A ≡
A Ʌ (B Ʌ C) Ʌ ¬B ≡
X V Y V ¬X V W ≡
¬(X Ʌ Y) V ¬Y V X ≡
(¬X Ʌ ¬Y) Ʌ X ≡

## Slide 6
Use the following rules to derive or simplify statements in Boolean algebra: De Morgan's Laws, distribution, association, commutation, double negation
Boolean algebra
Using a truth table, prove the law of absorption that: ¬X V (¬X Ʌ Y) ≡ ¬X
X | Y | ¬X | ¬X Ʌ Y | ¬X V (¬X Ʌ Y)

## Slide 7
Use the following rules to derive or simplify statements in Boolean algebra: De Morgan's Laws, distribution, association, commutation, double negation
Boolean algebra
Using a truth table, prove that (X V Y) V ¬(X Ʌ Y) is true.
X | Y | X V Y | ¬(X Ʌ Y) | (X V Y) V ¬(X Ʌ Y)

## Slide 8
Use the following rules to derive or simplify statements in Boolean algebra: De Morgan's Laws, distribution, association, commutation, double negation
Boolean algebra
Draw the circuit diagram for the expression: ¬(A Ʌ B) Ʌ (C V ¬D)

## Slide 9
Use the following rules to derive or simplify statements in Boolean algebra: De Morgan's Laws, distribution, association, commutation, double negation
Boolean algebra
There is one rule that is not in the specification, but can help.
Absorption allows for a second input to be removed if another one appears twice:
(A V B) Ʌ (A Ʌ ¬B) ≡ A
A V (A Ʌ B) ≡ A
A Ʌ (A V B) ≡ A