## Slide 1: Flip Flops and Adders
Boolean Algebra

## Slide 2: Adders and D-type flip-flops
Performing calculations using gates
With the right combination of gates, it is possible to output the result of a binary addition or subtraction including the value of any carry bit as a second output.
Half adders
A half adder can take an input of two bits and give a two-bit output as the correct result of an addition of the two inputs.
This is shown by the diagram above and represented by the truth table where S represents the sum and C represents the carry bit. S can be given as S = A ⊻ B, and C as C = A  B. Although a flip-flop can output the value of a carry bit, it only has two inputs so it cannot use the carry from a previous addition as a third input to a subsequent addition in order to add n-bit numbers.

## Slide 3: Full adders
A full adder combines two half adders to add three bits together including the two inputs A and B, and a carry bit C. The logic gate circuit below illustrates how two half adders have been connected with an additional OR gate to output the carry bit.

## Slide 4: Concatenating full adders
Multiple full adders can be connected together. Using this construct, n full adders can be connected together in order to input the carry bit into a subsequent adder along with two new inputs to create a concatenated adder capable of adding a binary number of n bits.
The four-bit adder is an example of a standard component that can be used in many applications involving arithmetic operations.

## Slide 5: Challenge
What would be the output S4 from a fifth adder connected to the diagram above if the inputs for A4 and B4 were 0 and 1? What would be the output C5?

## Slide 6: Challenge
What would be the output S4 from a fifth adder connected to the diagram above if the inputs for A4 and B4 were 0 and 1? What would be the output C5?
S4 = 1, C5 = 0

## Slide 7: D-type flip-flops
A flip flop is an elemental sequential logic circuit that can store one bit and flip between two states, 0 and 1. It has two inputs, a control input labelled 0 and a clock signal.
The clock or oscillator is another type of sequential circuit that changes state at regular time intervals,
Clocks are needed to synchronise the change of state of flip flop circuits.

## Slide 8: D-type flip-flops
The D-type flip-flop (D stands for Data or Delay) is a positive edge-triggered flip-flop, meaning that it can only change the output value from 1 to 0 or vice versa when the clock is at a rising or positive edge, i.e. at the beginning of a clock period.
When the clock is not at a positive edge, the input value is held and does not change. The flip-flop circuit is important because it can be used as a memory cell to store the state of a bit.

## Slide 9: D-type flip-flops
Output Q only takes on a new value if the value at D has changed at the point of a clock pulse.
This means that the clock pulse will freeze or 'store' the input value at D until the next clock pulse.
If D remains the same on the next clock pulse, the flip-flop will hold the same value.

## Slide 10: The use of a D type flip flop as a memory unit
A flip flop comprises several NAND (or AND and OR) gates and is effectively 1-bit memory. To store eight bits, eight flip-flops are required. Register memories are constructed by connecting a series of flip-flops in a row and are typically used for the intermediate storage needed during arithmetic operations. Static RAM is also created using D-type flip -flops. Imagine trying to assemble 16GB of memory in this way!

## Slide 11: The use of a D type flip flop as a memory unit
The graph below illustrates how the output Q only changes to match the input D in response to the rising edge on the clock signal. Q therefore delays, or 'stores ' the value of D by up to one clock cycle.

## Slide 12: Challenge

## Slide 13: Challenge